## Slide 1: Looking for the Maximum Independent Set: A New Perspective on the Stable Path Problem
Yichao Cheng1, Ning Luo1, Jingxuan Zhang1, 2, Timos Antonopoulos1, Ruzica Piskac1, Qiao Xiang3, 1,
1Yale University, 2Tongji University, 3Xiamen University
05/12/2021, IEEE INFOCOM’21

## Slide 2: What is the Stable Path Problem?
Powerful tool for BGP convergence analysis [1]
An undirected graph G=(V, E)
  n+1 nodes, node 0 represents the destination; a link represents neighborship
Each node i
  runs SPVP, an abstract version of BGP
  has a set of permitted paths
  has a ranking function to rank permitted paths
Stable path assignment: each node's selected path
  belongs to its permitted paths, and
  is a concatenation of the selected path of its neighbors
Stable path problem (SPP): does a stable path assignment exists?
[1] Griffin, Timothy, et al. "The Stable Paths Problem and Interdomain Routing." IEEE/ACM Transactions On Networking 10, no. 2 (2002): 232-243.

## Slide 3: Example: Good Gadget
A stable path assignment defines a tree rooted at node 0
Good gadget
Stable path assignment of good gadget

## Slide 4: Categories on SPP Instances
Safe: SPVP always converges, e.g., good gadget
Unique: has one and only one stable path assignment, e.g., good gadget and naughty gadget
Solvable: has at least one stable path assignment, e.g., disagree
Unsolvable: has no stable path assignment, e.g., bad gadget
naughty gadget
bad gadget
1
2
0
120
10
210
10
disagree

## Slide 5: Related Work on SPP
[2] Cittadini, Luca, et al. "On the Stability of Interdomain Routing." ACM Computing Surveys 44, no. 4 (2012): 1-40.
[3] Cittadini, Luca, et al. "From Theory to Practice: Efficiently Checking BGP Configurations for Guaranteed Convergence." IEEE Transactions on Network and Service Management 8, no. 4 (2011): 387-400.
[4] Gao, Lixin et al. "Stable Internet routing without global coordination." IEEE/ACM Transactions on networking 9, no. 6 (2001): 681-692.
Solvable
Unique
Safe
Greedy+-solvable [2, 3]
Dispute-wheel-free [1]
Gao-Rexford[4]
Unsolvable
Focus of this paper

## Slide 6: Why Focus on SPP Solvability?
Enable new interdomain routing use cases with more flexible policies
  E.g., collaborative interdomain routing [4], software-defined-interdomain routing [5]
Better understand the gap between solvable SPP and safe SPP
Help improve the efficiency of network configuration verification
[4] Pouryousef, Shahrooz, et al. "Towards Logically Centralized Interdomain Routing." In 17th USENIX Symposium on Networked Systems Design and Implementation (NSDI'20), pp. 739-757. 2020.
[5] Xiang, Qiao, et al. "Toward Optimal Software-Defined Interdomain Routing." In IEEE INFOCOM 2020-IEEE Conference on Computer Communications, pp. 1529-1538. IEEE, 2020.

## Slide 7: Outline
Background on SPP
Our Contribution

## Slide 8: Contribution: New SPP Solvability Results and Interdomain Use Cases
Theorem: A novel solvability digraph for reasoning SPP solvability
Algorithm: A polynomial-time heuristic solves more SPP than state-of-the-art
Use case: collaborative interdomain routing
Use case: privacy-preserving collaborative interdomain routing

## Slide 9: Outline
Background on SPP
Our Contribution
Solvability Digraph

## Slide 10: Properties of Stable Path Assignment
In a stable path assignment:
each node only has one path
each path's suffix must also be in the assignment
the stable path of each node is its most preferred one among the concatenation of the stable paths of all its neighbors
Good gadget
Stable path assignment for good gadget

## Slide 11: Solvability Digraph
Given an SPP instance, the corresponding solvability digraph is defined as:
Vertices: each vertex corresponds to a permitted path
Edges: 3 types of edges correspond to the 3 properties of SPP.
0
130
10
210
20
430
420
30
Type-1 edge (p1, p2): p1 and p2 from the same node's permitted paths, and p2 is more preferred
Type-2 edge (p1, p2): iff there exists a p3 such that (1) p2 and p3 are from the same node, and (2) p3 is a suffix of p1
Type-3 edge (p1, p2): iff there exists a p3 such that (1) p3 is from the same node as p1, but more preferred, and (2) p2 is a suffix of p3 and is 1-hop shorter.

## Slide 12: Solvability Graph - More Examples
Naughty Gadget
Bad Gadget

## Slide 13: Solvability Graph and SPP Solvability
Theorem 1: Given an SPP instance with n+1 nodes, it is solvable if and only if the corresponding solvability digraph has a maximum independent set of size n+1. (proof in the paper)
Good gadget
0
130
20
430
30
0
130
20
430
30
Naughty gadget
Bad gadget
No size-5 MIS

## Slide 14: Outline
Background on SPP
Our Contribution
Solvability Digraph
GreedyMIS: A Polynomial-Time Heuristic for SPP

## Slide 15: GreedyMIS: Basic Idea
Iteratively add nodes into an independent set of the solvability digraph
In each iteration:
  add path-vertices with no out edge, if none
  add one path-vertex if it is the only one left for the same node in SPP, if none
  randomly add one path-vertex with the lowest out degree
  remove all added path-vertices, their neighbors and all related edges from the digraph
Terminates when
  (solvable) one of size n+1 is found, or
  (non-solvable) no more nodes can be added into the set

## Slide 16: GreedyMIS: Example
Iteration 1: 0 is added (zero out edges)
Iteration 2: {120, 230, 340, 410} all have out degree of 1, randomly add 120 (one with lowest out degree)
Iteration 3: 340, 40 are added (zero out edges)
Iteration 4: 20 is added (zero out edges)
Final result: {0, 120, 340, 40, 20}
0
120
10
230
20
340
30
410
40
0
120
340
20
40

## Slide 17: GreedyMIS: Analysis
Theorem 2: Any SPP instance that is solvable by Greedy+ [3], , the best known polynomial-time heuristic algorithm for SPP, is also solvable by GreedyMIS. (proof in the paper)
Theorem 3: GreedyMIS solves strictly more SPP instances than Greedy+.
A direct result from Theorem 2 and the example in the last slide.

## Slide 18: Outline
Background on SPP
Our Contribution
Solvability Digraph
GreedyMIS: A Polynomial-Time Heuristic for SPP
Use Cases

## Slide 19: Use Case 1: Collaborative Interdomain Routing
Advantage: allow more flexible routing policies, i.e., doesn't haven't to be a "safe" SPP
Scenario: collaborative science networks such as Large Hadron Collider
AS
AS
AS
AS
AS
Route Control Server
(1) Collect AS policies
(3) Send back
stable path assignment
(2) Model and solve SPP using GreedyMIS

## Slide 20: Use Case 2: Privacy-Preserving, Collaborative Interdomain Routing
Scenario: multi-domain networks desire more flexible policies, but still want to keep policies private
Design: each AS exposes its export policies since it can be inferred, but keeps selection policy private
Protocol: an privacy-preserving version of GreedyMIS that employs linear secret sharing

## Slide 21: Outline
Background on SPP
Our Contribution
Solvability Digraph
GreedyMIS: A Polynomial-Time Heuristic for SPP
Use Cases
Performance Evaluation

## Slide 22: Performance Evaluation: Settings
Topology: real AS-level topologies from CAIDA Internet topology dataset
AS export policies: (1) C/P relationship, (2) blacklist ASes, (3) forbidden segments.
SPP instances: 11-50 ASes, 8-12k permitted paths
Comparison: GreedyMIS vs. Greedy [1] and Greedy+ [3]
Notes: Added earlier

## Slide 23: Results: Solvability of GreedyMIS
GreedyMIS solves all SPP instances in the experiment, while the other two algorithms solves less than 50%.

## Slide 24: Results: Efficiency of GreedyMIS
In 80% of the experiments, GreedyMIS solves SPP in no more than 0.01s

## Slide 25: Conclusion and Future Work
Propose the solvability digraph data structure to reason about SPP solvability
Design GreedyMIS, a polynomial-time heuristic that solves strictly more SPP instances than known state-of-the-art
Tailor GreedyMIS to important interdomain routing use cases
Demonstrate the efficiency and potentials of GreedyMIS via evaluation on real topologies
Future Work
Generic exact/approximated MIS algorithm for solving SPP
Apply the SPP-MIS theorem to network configuration verification

## Slide 26: Backup Slides

## Slide 27
path-digraph [3] and p-graph [4]
ss

## Slide 28: Solvability Digraph
Given an SPP instance, the corresponding solvability digraph is defined as:
Path-vertices: each vertex corresponds to a permitted path
Type-1 edge (p1, p2): p1 and p2 from the same node's permitted paths, and p2 is more preferred;
Type-2 edge (p1, p2): iff there exists a p3 such that (1) p2 and p3 are from the same node, and (2) p3 is a suffix of p1
Type-3 edge (p1, p2): iff there exists a p3 such that (1) p3 is from the same node as p1, but more preferred, and (2) p2 is a suffix of p3 and is 1-hop shorter.