## Slide 1: Network Layer: Global Internet Routing (Interdomain, BGP)
Qiao Xiang
https://qiaoxiang.me/courses/cnns-xmuf21/index.shtml
12/07/2021
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.

## Slide 2
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
        Distance vector protocols (distributed computing)
        Link state protocols (distributed state synchronization)
      Global Internet routing

## Slide 3: Admin
If you haven't done so, please let me and TA know your project topic as soon as possible
Final exam
  Similar format as midterm
  You still get to bring a cheatsheet
  Cover lectures 16-27
  17 + 1 (bonus) question

## Slide 4
Recap: Routing Context
Often depends on a graph abstraction:
graph nodes are routers
graph edges are physical links
  links have properties: delay, capacity, $ cost, policy
Goal: determine “good” paths
(sequences of routers) thru
networks from source to dest.
Routing
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5

## Slide 5: Recap: Routing Computation using Distance Vector/Bellman-Ford Routing
Distributed computation: At node i, computes
One way to understand BFA is to consider it as a dynamic programming alg, propagating from dest to other nodes
i
j
destination

## Slide 6: Recap: Fixing DV/BFA
Property of BFA
  Bad news may propagate slowly due to loops
Techniques
  Reverse poison
    Avoid two-node loops
  DSDV
    Using destination seq to partition into epochs
    A good example of analysis using global invariants
  Diffusive Update Alg (DUAL)
    Utilize backup routes

## Slide 7: Recap: Link State Routing
Basic idea: instead of distributed computing of routes, only distributed state distribution (synchronization)
Link state distribution can still have much complexity, e.g.,
  out of order delivery
  partition and reconnect
  scalability
Notes:   Simplicity
  churns before convergence
    path exploration; counting-to-infinity
  not enough information when making routing decision (only next-hops and their distance estimates)
While distance-vector protocols are appropriate for small internetworks, and require much less configuration and management
- IGRP was a significant improvement over RIP, which had a hop count restriction that limited the size of an internetwork. IGRP supports internetworks with up to 255 hops.
IGRP:
Upon router startup, IGRP broadcast request messages to other routers. Upon receipt of the message, router send their routing tables to the startup router. Routing tables contain entries for each of the networks that a router can reach. At regular intervals, routers automatically transmit their routing tables to other routers which in turn update their own routing tables if there are changes in the topology. A triggered update occurs if the network topology changes. Triggered updates allow quick responses to changes in the network. When routers add entries to routing tables, 1 is added to the hop count to account for the hop between the router and the neighbor from which it received the route information. When a route is entered into the routing table, a timer is set. As routing table updates arrive and a route entry is verified to still be valid, the timer is reset. If a known router fails to appear in an update and in subsequent updates, the timer will run out and the route entry will be purged.

## Slide 8: Roadmap: Routing Computation Architecture Spectrum
Datapath
Distributed Bellman Ford
Distributed Link State
Dijkstra
Datapath
Distributed Bellman Ford
Datapath
Distributed Bellman Ford
Distributed Link State
Distributed Link State
Dijkstra
Dijkstra
Notes: RIP: 1988 RFC1058 OSFPv2: RFC2328

## Slide 9
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
        Distance vector protocols (distributed computing)
        Link state protocols (distributed state synchronization)
      Global Internet routing

## Slide 10: Exercise
Does it work to use DV or LS as we discussed for global Internet routing?
Notes: DV: so many loops,
LS/DV: scalability

## Slide 11: Requirements and Solution of Current Global Internet Routing
Scalability: handle network size (#devices) much higher than typical DV or LS can handle
  Solution: Introduce new abstraction to reduce network (graph) size
Autonomy: allow each network to have individual preference of routing (full control of its internal routing; control/preference of routing spanning multiple networks)
  Solution: hierarchical routing and policy routing
Notes: Other than scale, what else?

## Slide 12: New Abstraction: Autonomous Systems (AS)
Abstract each network as an autonomous system (AS), identified by an AS number (ASN)
Conceptually the global routing graph consists of only autonomous systems as nodes
http://www.bgplookingglass.com/list-of-autonomous-system-numbers

## Slide 13
Routing with Autonomous Systems
Internet routing is divided into intra-AS routing and inter-AS routing
  Intra-AS routing (also called intradomain routing)
    A protocol running insides an AS is called an Interior Gateway Protocol (IGP), each AS can choose its own protocol, such as RIP, E/IGRP, OSPF, IS-IS
  Inter-AS routing (also called interdomain routing)
    A protocol runs among autonomous systems is also called an Exterior Gateway Protocol (EGP)
    The de facto EGP protocol is BGP

## Slide 14
b
a
AS C
(RIP intra
routing)
c
AS B
(OSPF intra
routing)
AS A
(OSPF intra
routing)
eBGP
iBGP
Gateway routers participate in intradomain to learn internal routes.
Gateway routers of diff. auto. systems exchange routes using eBGP
Gateway routers of same AS share learned external routes using iBGP.
i
e
f
g
h
d
Inter-AS routers form an overlay
Routing with Autonomous Systems

## Slide 15: Routing with Autonomous Systems
a
b
b
a
a
C
A
B
d
c
A.a
A.c
C.b
B.a
c
b
border (exterior gateway) routers
interior (gateway) routers

## Slide 16: Summary: Internet Routing Architecture
Autonomous systems have flexibility to choose their own intradomain routing protocols
  allows autonomy
Only a small # of routers (gateways) from each AS in the interdomain level
  improves scalability
Interdomain routing using AS topology instead of detailed topology
  improves scalability/privacy

## Slide 17
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
      Global Internet routing
        Basic architecture
        BGP (Border Gateway Protocol): The de facto Inter-domain routing standard

## Slide 18
BGP Basic Operations
BGP is a Path Vector protocol
  similar to Distance Vector protocol
  a border gateway sends to a neighbor entire path (i.e., a sequence of ASNs) to a destination, e.g.,
    gateway X sends to neighbor N its path to dest. Z:
path (X,Z) = X,Y1,Y2,Y3,…,Z
  if N selects path(X, Z) advertised by X, then: path (N,Z) = N, path (X,Z)
X
N
Z

## Slide 19
BGP Basic Operations
Establish session on
TCP port 179
Exchange all
active routes
Exchange incremental
updates
AS1
AS2
while (connection is ALIVE) exchange UPDATE message select best available route
if route changes, export to neigh.
BGP session

## Slide 20: BGP Messages
Four types of messages
  OPEN: opens TCP connection to peer and authenticates sender
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 21
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
      Global Internet routing
        Basic architecture
        BGP (Border Gateway Protocol): The de facto Inter-domain routing standard
          Basic operations
          BGP as a policy routing framework (control interdomain routes)

## Slide 22
BGP Policy Routing Framework:
Label Route Information Sources
Forwarding Information Base (FIB)
OSPF
domain
RIP
domain
BGP
OS kernel
RIP process
RIP routing table
Routing Information Base (RIB)
OSPF process
OSPF Routing table
BGP process
BGP routing table
22

## Slide 23: BGP Policy Routing Framework: Decision Components
routing cache
select best path
export path to neighbors
route selection policy: rank paths
export policy: which paths export to which neighbors
Yale
Qwest
AT&T
Internet2
1 3 0
1 0
23

## Slide 24: BGP Example (1)
AS A
(OSPF)
AS B
(OSPF intra
routing)
AS D
AS C
i
b
b->i: I can reach hosts
in D; my path: BCD
a1
a2
d
d->a2: I can reach
hosts in D; my path: D
a1->i: I can reach hosts in D; my path: AD
E
F
Export to E: i->e: I can reach hosts in D; path: IAD
AS I
a2->a1: I can reach
hosts in D; path: D
Route selection policy:
- Shortest AS Path policy:
b->i2: I can reach hosts
in D; my path: BCD
i2
i2->i: I can reach hosts in D; path: BCD
No export to F (effect?)
Choose AD using a1
Export policy controls ingress, i.e., who can use I
Notes: Choose

## Slide 25: BGP Example (2)
AS A
(OSPF)
AS B
(OSPF intra
routing)
AS D
AS C
i
b
b->i: I can reach hosts
in D; my path: BCD
a1
a2
d
d->a2: I can reach
hosts in D; my path: D
a1->i: I can reach hosts in D; my path: AD
E
F
Export to E: i->e: I can reach hosts in D; path: IBCD
AS I
a2->a1: I can reach
hosts in D; path: D
Selection policy: - Low local_pref for A
- Shortest AS Path
- Prefer eBGP
b->i2: I can reach hosts
in D; my path: BCD
i2
i2->i: I can reach hosts in D; path: BCD
Outcome: Choose BCD using b
Called hot potato (why?)
Notes: Choose

## Slide 26: BGP Example (3)
AS A
(OSPF)
AS B
(OSPF intra
routing)
AS D
AS C
i
b
b->i: I can reach hosts
in D; my path: BCD
a1
a2
d
d->a2: I can reach
hosts in D; my path: D
a1->i: I can reach hosts in D; my path: AD
E
F
Export to E: i->e: I can reach hosts in D; path: IBCD
AS I
a2->a1: I can reach
hosts in D; path: D
Selection policy: - Low local pref A
- Shortest AS Path
- Prefer iBGP
b->i2: I can reach hosts
in D; my path: BCD
i2
i2->i: I can reach hosts in D; path: BCD
Outcome: Choose BCD using i2
Called cold potato (why?)
Notes: Choose

## Slide 27: Observing BGP Paths
Using one of the looking glass servers: http://www.bgp4.as/looking-glasses
https://www.gin.ntt.net/looking-glass/

## Slide 28
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
      Global Internet routing
        Basic architecture
        BGP (Border Gateway Protocol): The de facto Inter-domain routing standard
          Basic operations
          BGP as a policy routing framework (control interdomain routes)
          Policy/interdomain routing analysis

## Slide 29
Motivation: Policy Routing Stability
2
0
3
1
2 1 0
2 0
1 3 0
1 0
3 2 0
3 0
4
3
preferred
less
preferred
The BAD GADGET example:
- 0 is the destination
- the route selection policy of each AS is to prefer its counter clock-wise neighbor
Policy (preferences) aggregation fails: routing instability !
A policy routing system can be considered as a system to aggregate local preferences, but aggregation may not be always successful.

## Slide 30: General Framework of Preference Aggregation
Also called Social Choice
  Given individual preferences, define a framework to aggregate individual preferences:
    A set of choices: a, b, c, …
    A set of voters 1, 2, …
      Each voter has a preference (ranking) of all choices, e.g.,
        voter 1: a > b > c
        voter 2: a > c > b
        voter 3: a > c > b
    A well-specified aggregation rule (protocol) computes an aggregation of ranking, e.g.,
      Society (network): a > b > c
Notes: https://en.wikipedia.org/wiki/Arrow%27s_impossibility_theorem

## Slide 31: Example: Aggregation of Global Preference
S
A
B
D
Choices (for S->D route): SAD, SBD, SABD, SBAD
Voters S, A, B, D
Each voter has a preference, e.g.,
  S: SAD > SBD > SABD > SBAD
  …
Notes: https://en.wikipedia.org/wiki/Arrow%27s_impossibility_theorem

## Slide 32: Arrow’s Aggregation Framework
Axioms:
  Transitivity
    if a > b & b > c, then a > c
  Unanimity:
    If all participants prefer a over b (a > b) => a > b
  Independence of irrelevant alternatives (IIA)
    Social ranking of a and b depends only on the relative ranking of a and b among all participants
Result:
  Arrow’s Theorem: Any constitution that respects transitivity, unanimity and IIA is a dictatorship.
Notes: https://en.wikipedia.org/wiki/Arrow%27s_impossibility_theorem

## Slide 33: Proofs of Arrow’s Theorem
There are quite a few proofs, and the six-page paper linked on the Schedule page gives three simple proofs.
Below, I give the key insight of the proof using approach 1.

## Slide 34: The Extremal Lemma
Let choice b be chosen arbitrarily. Assume that every voter puts b at the very top or the very bottom of his ranking. Then society must as well (even if half voters put b at the top and half at the bottom)
Proof: by contradiction.
  Assume there exist a and c such that society has a >= b; b >= c.
    By transitivity, a >= c
  We can move c above a w/o changing ab or cb votes, leading to c > a
    By unanimity, c > a

## Slide 35: Step 1: Existence of Pivotal Voter
Let choice b be chosen arbitrarily. There exist a voter n* = n(b) who is extremely pivotal for b in the sense that by changing his vote at some profile, he can move b from the very bottom to the very top in the social ranking.
Proof:
  Consider an extreme profile where b is at the bottom of each voter.
  Consider voter from 1 to n, and we move b from bottom to top one-by-one.
  The first voter whose change causes b to move to the top is n*
    By unanimity, this change must happen at the latest when n*=n

## Slide 36: Step 2: n*=n(b) is dictator of any pair ac not involving b
Proof
  Consider a from ac pair. We show that if a >n* c, then constitution protocol has a > c
  Let profile before n* moves b to top as profile I
  Let profile after n* moves b to top as profile II
  Construct profile III from II by letting n* move a above b; all others can arrange ac as they want, but leave b in extreme position
    a>b in profile I, and a,b is equivalent by IIA in profiles I and III
    b>c in profile II, and bc is equivalent by IIA in profiles II and III
b
.
.
.
b
.
.
.
.
.
.
b
.
.
.
b
.
.
.
b
b
.
.
.
b
.
.
.
b
.
.
.
.
.
.
b
.
.
.
b
1 2 n* . N
b
.
.
.
b
.
.
.
a
b
.
c
.
.
.
b
.
.
.
b
Constitution protocol: b bottom
Constitution protocol : b top
Profile I
Profile II
Profile III
Constitution protocol: a > b since ab same as I
b > c since bc same as II

## Slide 37: Step 3: n* is dictator for every pair ab
Consider c not equal to a or b
There exists n(c) who is a dictator of any pair not involving c, such as the pair ab, i.e.,
  For any profile, if a >n(c) > b, a > b in constitution protocol
n(c) must be n*
  Assume not.
    Consider Profile I and Profile II.
    Since n(c) is not n*, n(c) ranking of ab does not change in Profile I and Profile II.
    When n* changes ab ranking between Profile I and Profile II, the global ranking of ab changes.
    Contradiction.

## Slide 38
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
      Global Internet routing
        Basic architecture
        BGP (Border Gateway Protocol): The de facto Inter-domain routing standard
          Basic operations
          BGP as a policy routing framework (control interdomain routes)
          Policy/interdomain routing analysis
            Global preference aggregation and Arrow’s Theorem
            Local preference aggregation

## Slide 39: BGP w/ Local Preference
BGP preferences are typically local (only on paths start from itself)
Hence the preferences have dependency (priority)
  The “closer” a node to the destination, the more “powerful” it may be
2 1 0
2 0
1 0
3 0
1 3 0
3 2 0
2
0
1
3
320
30
210
20
130
10

## Slide 40: Complete Dependency: P-Graph
Complete dependency can be captured by a structure called P-graph
Nodes in P-graph are feasible paths
Edges represent priority (low to high)
  A directed edge from path N1P1 to P1
    intuition: to let N1 choose N1P1, P1 must be chosen and exported to N1
  A directed edge from a lower ranked path to a higher ranked path
    intuition: the higher ranked path should be considered first
2 1 0
2 0
1 0
3 0
1 3 0
3 2 0
2
0
1
3
320
30
210
20
130
10
Any observation on the P-graph?

## Slide 41: P-Graph and BGP Convergence
If the P-graph of the networks has no loop, then policy routing converges.
  intuition: choose the path node from the partial order graph with no out-going edge to non-fixed path nodes, fix the path node, eliminate all no longer feasible; continue
Example: suppose we swap the order of 30 and 320
2 1 0
2 0
1 0
3 0
1 3 0
3 2 0
2
0
1
3
30
320
210
20
130
10