## Slide 1: A Taxonomy of Communication Networks
  Y. Richard Yang
  http://zoo.cs.yale.edu/classes/cs433/
  09/05/2017

## Slide 2
Outline
Admin and recap
A taxonomy of communication networks

## Slide 3: Admin
Please check the Schedule page for links to related readings

## Slide 4: Recap
A protocol defines the format and the order of messages exchanged between two or more communicating entities, as well as the actions taken on the transmission or receipt of a message or other events.
Key Internet milestones and their implications:
  ARPANET is sponsored by ARPA 
  The initial IMPs (routers) were made by a small company 
  Many networks 
  Commercialization 
design should survive failures
  internetworking: need a network to connect networks
keep the network simple
  architecture supporting decentralized, autonomous systems

## Slide 5: Recall: Internet Physical Infrastructure
Backbone ISP
ISP
ISP
Residential access, e.g.,
  Cable, Fiber, DSL, Wireless
Campus access, e.g.,
  Ethernet, Wireless
The Internet is a network of networks
Each individually administrated network is called an Autonomous System (AS)
  ~ 58000 ASes; Avg 5.7 hops; (http://bgp.potaroo.net/as2.0/bgp-active.html)
data center

## Slide 6: Observing the Internet State
Read the manual of traceroute, and try it on a zoo machine
  % /usr/sbin/traceroute <machine_name>
Look at the web sites of the routers you see through traceroute
Lookup ASN info
  https://www.ultratools.com/tools/asnInfo
Routeviews to see connection info (e.g., neighbors) about a network: https://www.ripe.net/analyse/internet-measurements/routing-information-service-ris/routing-information-service-ris

## Slide 7
Roadmap
So far we have looked at only the topology and physical connectivity of the Internet: a mesh of computers interconnected via various physical media
A basic question: how are data (the bits) transferred through communication networks?

## Slide 8: Outline
Admin. and recap
A taxonomy of communication networks

## Slide 9: Taxonomy of Communication Networks
Broadcast networks
  nodes share a common channel; information transmitted by a node is received by all other nodes in the network
  examples: TV, radio
Switched networks
  information is transmitted to a small sub-set (usually only one) of the nodes
communication networks
broadcast networks
switched networks

## Slide 10
Circuit switching: dedicated circuit per call/session:
  e.g., telephone, cellular voice
Packet switching: data sent thru network in discrete “chunks”
  e.g., Internet, cellular data
A Taxonomy of Switched Networks
communication networks
switched networks
broadcast networks
circuit-switched networks (e.g., telephone)
packet-switched networks (e.g., Internet)

## Slide 11
Outline
Admin. and review
A taxonomy of communication networks
  circuit switched networks

## Slide 12
Circuit Switching
Each link has a number of “circuits”
  sometime we refer to a “circuit” as a channel or a line
An end-to-end connection reserves one “circuit” at each link
First commercial telephone switchboard was opened in 1878 to serve the 21 telephone customers in New Haven
Notes: http://www.classicrotaryphones.com/new-england-operators2_big.jpg

## Slide 13
Circuit Switching: Resources/Circuits (Frequency, Time and others)
Divide link resource into “circuits”
  frequency division multiplexing (FDM)
  time division multiplexing (TDM)
  others such as code division multiplexing (CDM), color/lambda division

## Slide 14: Circuit Switching: The Process
Three phases
  circuit establishment
  data transfer
  circuit termination

## Slide 15
circuit establishment
DATA
data transmission
circuit termination
Host A
Host B
Node 1
Node 2
propagation delay
from A to Node 1
propagation delay
from B To A
processing delay at Node 1
Timing Diagram of Circuit Switching

## Slide 16
Delay Calculation in Circuit Switched Networks
Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x105 km/sec)
Propagation delay: delay for the first bit to go from a source to a destination
DATA
prop. delay: d/s

## Slide 17
Delay Calculation in Circuit Switched Networks
Transmission delay:
R = reserved bandwidth (bps)
L = message length (bits)
DATA
d/s
trans. delay = L/R
Transmission delay: time to pump data onto link at line rate

## Slide 18: An Example
Propagation delay
  suppose the distance between A and B is 4000 km, then one-way propagation delay is:
Transmission delay
  suppose your iphone reserves a one-slot HSCSD channel
    each HSCSD frame can transmit about 115 kbps
    a frame is divided into 8 slots
  then the transmission delay of using one reserved slot for a message of 1 Kbits:

## Slide 19: An Example (cont.)
Suppose the setup message is very small, and the total setup processing delay is 200 ms
Then the delay to transfer a message of 1 Kbits from A to B (from the beginning until host receives last bit) is:
DATA
20 + 200
20
20
70

## Slide 20
Outline
Admin. and review
A taxonomy of communication networks
  circuit switched networks
  packet switched networks

## Slide 21
Packet Switching
Each end-to-end data flow (i.e., a sender-receiver pair) divided into packets
Packets have the following structure:
    header and trailer carry control information (e.g., destination address, check sum)
    where is the control information for circuit switching?
At each node the entire packet is received, processed (e.g., routing), stored briefly, and then forwarded to the next node; thus packet-switched networks are also called store-and-forward networks. On its turn, a packet uses full link bandwidth
Header
Data
Trailer

## Slide 22
Packet Switching

## Slide 23
Inside a Packet Switching Router
An output queueing switch
incoming links
outgoing links
node
Memory

## Slide 24
Outline
Admin. and review
A taxonomy of communication networks
  circuit switched networks
  packet switched networks
  circuit switching vs. packet switching

## Slide 25
Packet Switching vs. Circuit Switching
The early history of the Internet was a heated debate between Packet Switching and Circuit Switching
  the telephone network was the dominant network
Need to compare packet switching with circuit switching

## Slide 26: Circuit Switching vs. Packet Switching
 | circuit switching | packet switching
resource usage | use a single partition bandwidth | use whole link bandwidth
reservation/setup | need reservation (setup delay) | no reservation
resource contention | busy signal (session loss) | congestion (long delay and packet losses)
charging | time | packet
header | no per-pkt header | per packet header
fast path processing | fast | per packet processing

## Slide 27: Circuit Switching vs. Packet Switching
 | circuit switching | packet switching
resource usage | use a single partition bandwidth | use whole link bandwidth
reservation/setup | need reservation (setup delay) | no reservation
resource contention | busy signal (session loss) | congestion (long delay and packet losses)
charging | time | packet
header | no per-pkt header | per packet header
fast path processing | fast | per packet processing

## Slide 28: Key Issue to be Settled
A key issue: what is the efficiency of resource partition?
Tool used to analyze the issue: queueing theory
  Some basic results of queueing theory can be quite useful in many systems settings
10G
5G
5G
Notes: 10M bps link and 10 flows: partition into 10 1 Mbps or

## Slide 29
Outline
Admin. and review
A taxonomy of communication networks
  circuit switched networks
  packet switched networks
  circuit switching vs. packet switching
  M/M queues and statistical multiplexing

## Slide 30: Queueing Theory
Strategy:
  model system state
    if we know the fraction of time that the system spends at each state, we can get answers to many basic questions: how long does a new request need to wait before being served?
System state changes upon events:
  introduce state transition diagram
  focus on equilibrium: state trend neither growing nor shrinking (key issue: how to define equilibrium)
Our approach: We are not interested in extremely precise modeling, but want quantitative intuition

## Slide 31: Warm up: Analysis of Circuit-Switching Blocking (Busy) Time
Assume a link has only a finite number of N circuits
Objective: compute the percentage of time that a new session (call) is blocked
Analogy in a more daily-life scenario?
Key parameters?
Notes: Key input parameters?

## Slide 32: Analysis of Circuit-Switching Blocking (Busy) Time
Consider a simple arrival pattern
  client requests arrive at a rate of  (lambda/second)
  service rate: each call takes on average 1/ second
Arrival and service patterns: memoryless (Markovian)
  During a small interval t, the number of expected new arrivals is: t
  During a small interval t, the chance (fraction) of a current call finishes is: t
This model is also called an M/M/N model

## Slide 33: Analysis of Circuit-Switching Blocking (Busy) Time: State
k+1
system state: # of busy lines
0
1
k
N
p0
p1
pk
pk+1
pN
Q: How to characterize equilibrium?

## Slide 34: Equilibrium = Time Reversibility [Frank Kelly]
Statistically cannot distinguish
time
state
k
k+1

## Slide 35: Analysis of Circuit-Switching Blocking (Busy) Time: Sketch
0
1
k
N
system state: # of busy lines
at equilibrium (time resersibility) in one unit time: #(transitions k  k+1) = #(transitions k+1  k)
p0
p1
pk
k+1
pk+1

(k+1)
pN

## Slide 36: Queueing Analysis: Packet Switching Delay
Four types of delay at each hop
  nodal processing delay: check errors & routing
  queueing: time waiting for its turn at output link
  transmission delay: time to pump packet onto a link at link speed
  propagation delay: router to router propagation
The focus is on queueing and transmission delay
system state?

## Slide 37: Packet Switching Delay
0
1
k
N
system state: #packets in queue
at equilibrium (time reversibility) in one unit time: #(transitions k  k+1) = #(transitions k+1  k)
p0
p1
pk
k+1
pk+1

