## Slide 1: Network Transport Layer: TCP Connection Management, Congestion Control
Qiao Xiang
https://qiaoxiang.me/courses/cnns-xmuf21/index.shtml
11/18/2021
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.

## Slide 2: Admin
Lab assignment 5 to be posted tomorrow
Class Project
  15% of your final score
  Please start ASAP
  Talk to the instructor or TA to get feedback
  Send your topic and team member list to TA

## Slide 3
Recap: Reliable Transport
Basic structure: sliding window protocols
Realization: GBN or SR
General technique: pipelining.

## Slide 4: Recap: TCP Reliable Data Transfer
Connection-oriented:
  connection management
    setup (exchange of control msgs) init’s sender, receiver state before data exchange
    close
Full duplex data:
  bi-directional data flow in same connection
A sliding window protocol
  a combination of go-back-n and selective repeat:
    send & receive buffers
    cumulative acks
    TCP uses a single retransmission timer
    do not retransmit all packets upon timeout

## Slide 5: Recap: TCP Segment Structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
rcvr window size
ptr urgent data
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
RST, SYN, FIN:
connection management
(reset, setup teardown
commands)
flow control
ACK: ACK #
valid
counting
by bytes
of data
(not segments!)
Also in UDP
URG: urgent data
(generally not used)
PSH: push data now
(generally not used)

## Slide 6
Recap: TCP Seq. #’s and ACKs
Seq. #’s:
  byte stream “number” of first byte in segment’s data
ACKs:
  seq # of next byte expected from other side
  cumulative ACK in standard header
  selective ACK in options
Host A
Host B
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=42, ACK=80
User
types
‘C’
host ACKs
receipt
of echoed
‘C’
host ACKs
receipt of
‘C’, echoes
back ‘C’
time
simple telnet scenario

## Slide 7
Recap: TCP Reliable Data Transfer
Basic structure: sliding window protocol
Remaining issue: How to determine the “right” parameters?
  timeout value
  sliding window size?
Timeout = EstRTT + 4 * DevRTT
EstRTT = (1-alpha)*EstRTT + alpha*SampleRTT

## Slide 8: Recap: Fast Retransmit
Issue: Timeout period often relatively long:
  long delay before resending lost packet
Question: Can we detect loss faster than RTT?
If sender receives 3 ACKs for the same data, it supposes that segment after ACKed data was lost:
  resend segment before timer expires
Detect lost segments via duplicate ACKs
  sender often sends many segments back-to-back
  if segment is lost, there will likely be many duplicate ACKs

## Slide 9
Outline
Admin and Recap
TCP reliability
  data seq#, ack, buffering
  timeout realization
  connection management

## Slide 10: Why Connection Setup/When to Accept (Safely Deliver) First Packet?
sender
receiver
ACK for 0
accept
data 0
10

## Slide 11: Why Connection Setup/When to Accept (Safely Deliver) First Packet?
sender
receiver
ACK for 0 (n)
accept
data 0 (transfer $1000 to B)
data 0 (transfer $1000 to B)
accept?
11
Notes: a sender should not reuse a seq# before it is sure the packet has left the network

## Slide 12: Recap: Transport “Safe-Setup” Principle
A general safety principle for a receiver R to accept a message from a sender S is the general “authentication” principle, which consists of two conditions:
  Transport authentication principle:
  [p1] Receiver can be sure that what Sender says is fresh
  [p2] Receiver receives something that only Sender can say
We first assume a secure setting: no malicious attacks.
Exercise: Techniques to allow a receiver to check for freshness (e.g., add a time stamp)?

## Slide 13: Generic Challenge-Response Structure Checking Freshness
sender
receiver
Challenge (nonce)
deliver
I have data to send
Demonstrate knowing nonce; data

## Slide 14: Three Way Handshake (TWH) [Tomlinson 1975]
Host A
SYN(seq=x)
Host B
ACK(seq=x), SYN(seq=y)
ACK(seq=y)
DATA(seq=x+1)
SYN: indicates connection setup
accept data only after
verified y is bounced back
x is the init. seq
notify initial seq#. Accept?
think of y as a challenge
Notes: Syn(seq=x) could be duplicate or malicious

## Slide 15: Scenarios with Duplicate Request/SYN Attack
Host A
Host B
ACK(seq=x), SYN(seq=y)
REJECT(seq=y)
SYN(seq=x)
accept?
no such request
reject

## Slide 16: Scenarios with Duplicate Request/SYN Attack
Host A
Host B
ACK(seq=x), SYN(seq=y)
REJECT(seq=y)
SYN(seq=x)
accept?
no such request
reject
ACK(seq=z)

## Slide 17: Make “Challenge y” Robust
To avoid that “SYNC ACK y” comes from reordering and duplication
  for each connection (sender-receiver pair), ensuring that two identically numbered packets are never outstanding at the same time
    network bounds the life time of each packet
    a sender will not reuse a seq# before it is sure that all packets with the seq# are purged from the network
    seq. number space should be large enough to not limit transmission rate
Increasingly move to cryptographic challenge and response
Notes: Add QUIC design: QUIC uses a cryptographic handshake
  Servers
    front-end servers, which collectively handle billions of requests a day from web browsers and mobile apps across a wide range of services.
  On the client side, we have deployed QUIC in
    Chrome,
    our mobile video streaming YouTube app, and in the
    Google Search app on Android
TCP connections commonly incur at least one round-trip delay of connection setup time before any application data can be sent, and TLS adds two round trips to this delay

## Slide 18: Connection Close
Why connection close?
  so that each side can release resource and remove state about the connection (do not want dangling socket)
client
server
I am done. Are you done too?
I am done too. Goodbye!
init. close
close
close
release
resource?
release
resource?
release
resource?

## Slide 19: General Case: The Two-Army Problem
The gray (blue) armies need to agree on whether or not they will attack the white army. They achieve agreement by sending messengers to the other side. If they both agree, attack; otherwise, no. Note that a messenger can be captured!

## Slide 20: Time_Wait
Generic technique: Timeout to “solve” infeasible problem
  Instead of message-driven state transition, use a timeout based transition; use timeout to handle error cases
client
server
I am done. Are you done too?
I am done too. Goodbye!
init. close
close
close
release
resource?
release
resource?
release
resource?
Closed
Working
Time_Waiit
Working
Closed

## Slide 21: Time_Wait Design Options
Time to retransmit ACK
Host A
FIN
Host B
ACK
close
Design 2 (receiver time wait)
Close after first ACK
All states removed
All states removed
Host A
FIN
Host B
ACK
close
Time = n x timeout
Time to retry FIN after each timeout
Design 1 (initiator time wait)
Close after receive FIN
All states removed
All states removed

## Slide 22: TCP Four Way Teardown (For Bi-Directional Transport)
Host A
FIN
Host B
ACK
ACK
FIN
close
close
closed
all states removed
timed wait
can retransmit the ACKif its ACK is lost
closed
A->B closed
A->B closed
all states removed
propose close A->B
propose close B->A

## Slide 23
%netstat -t -a
CLOSED
LISTEN
SYN RCVD
SYN
SYN/ACK
ACK
CLOSED
SYN SENT
ESTABLSIHED
ESTABLSIHED
FIN
ACK
ACK
FIN WAIT 1
ESTABLSIHED
ESTABLSIHED
CLOSE WAIT
FIN
LAST ACK
FIN WAIT 2
TIME WAIT

## Slide 24: TCP Connection Management
TCP lifecycle: init SYN/FIN
CLOSED
SYN RCVD
SYN
SYN/ACK
ACK
CLOSED
SYN SENT
ESTABLSIHED
FIN
ACK
ACK
FIN WAIT 1
ESTABLSIHED
ESTABLSIHED
CLOSE WAIT
FIN
LAST ACK
FIN WAIT 2
TIME WAIT
http://dsd.lbl.gov/TCP-tuning/ip-sysctl-2.6.txt

## Slide 25: TCP Connection Management
TCP lifecycle: wait for SYN/FIN
CLOSED
SYN RCVD
SYN
SYN/ACK
ACK
CLOSED
SYN SENT
ESTABLSIHED
FIN
ACK
ACK
FIN WAIT 1
ESTABLSIHED
ESTABLSIHED
CLOSE WAIT
FIN
LAST ACK
FIN WAIT 2
TIME WAIT

## Slide 26
A Summary of Questions
Basic structure: sliding window protocols
How to determine the “right” parameters?
  timeout: mean + variation
  sliding window size?

## Slide 27
Sliding Window Size Function: Rate Control
Transmission rate determined by congestion window size, cwnd, over segments:
cwnd segments, each with MSS bytes sent in one RTT:
Rate =
cwnd * MSS
RTT
Bytes/sec
cwnd
Assume W is small enough. Ignore small details. MSS: Minimum Segment Size

## Slide 28
Some General Questions
Big picture question:
How to determine a flow’s sending rate?
For better understanding, we need to look at a few basic questions:
What is congestion (cost of congestion)?
Why are desired properties of congestion control?

## Slide 29
Roadmap
What is congestion
The basic CC alg
TCP/reno CC
TCP/Vegas
A unifying view of TCP/Reno and TCP/Vegas
Network wide resource allocation
  Framework
  Axiom derivation of network-wide objective function
  Derive distributed algorithm

## Slide 30
Outline
Admin and recap
TCP Reliability
Transport congestion control
  what is congestion (cost of congestion)

## Slide 31
flow 2 (5 Mbps)
flow 1
router 1
router 2
10 Mbps
5 Mbps
20 Mbps
Cause/Cost of Congestion: Single Bottleneck
- Flow 2 has a fixed sending rate of 5 Mbps
- We vary the sending rate of flow 1 from 0 to 20 Mbps
- Assume
  no retransmission; link from router 1 to router 2 has infinite buffer
20 Mbps
20 Mbps
throughput: e2e packets delivered in unit time
Delay?
sending rate by flow 1 (Mbps)
throughput of flow 1 & 2 (Mbps)
5
10
5
0
sending rate by flow 1 (Mbps)
delay at central link
5
0
delay due to
randomness

## Slide 32
flow 2 (5 Mbps)
flow 1
router 1
10 Mbps
5 Mbps
20 Mbps
Cause/Cost of Congestion: Single Bottleneck
Assume
  no retransmission
  the link from router 1 to router 2 has finite buffer
  throughput: e2e packets delivered in unit time
20 Mbps
20 Mbps
Zombie packet: a packet dropped at the link from router 2 to router 5; the upstream transmission from router 1 to router 2 used for that packet was wasted!
router 3
router 4
router 2
router 5
router 6
sending rate by flow 1 (Mbps)
throughput of flow 1 & 2 (Mbps)
5
10
5
0
x

## Slide 33
Summary: The Cost of Congestion
When sources sending rate too high for the network to handle”:
Packet loss =>
  wasted upstream bandwidth when a pkt is discarded at downstream
  wasted bandwidth due to retransmission (a pkt goes through a link multiple times)
High delay
Load
Load
Delay
Throughput
knee
cliff
congestion
collapse
packet
loss

## Slide 34
Outline
Admin and recap
TCP Reliability
Transport congestion control
  what is congestion (cost of congestion)
  basic congestion control alg.

## Slide 35
Window-based:
Congestion control by controlling the window size of a sliding window, e.g., set window size to 64KBytes
Example: TCP
Rate-based:
Congestion control by explicitly controlling the sending rate of a flow, e.g., set sending rate to 128Kbps
Example: ATM
Discussion: rate-based vs. window-based
Rate-based vs. Window-based

## Slide 36
Sliding Window Size Function: Rate Control
Transmission rate determined by congestion window size, cwnd, over segments:
cwnd segments, each with MSS bytes sent in one RTT:
Rate =
cwnd * MSS
RTT
Bytes/sec
cwnd
Assume W is small enough. Ignore small details. MSS: Maximum Segment Size

## Slide 37
Window-based Congestion Control
Window-based congestion control is self-clocking: considers flow conservation, and adjusts to RTT variation automatically.
Hence, for better safety, more designs use window-based design.

## Slide 38
The Desired Properties of a Congestion Control Scheme
Efficiency: close to full utilization but low delay
  fast convergence after disturbance
Fairness (resource sharing)
Distributedness (no central knowledge for scalability)

## Slide 39: Derive CC: A Simple Model
User 1
User 2
User n
sum xi
d = sum xi > Xgoal?
x1
x2
xn
Flows observe congestion signal d, and locally take actions to adjust rates.

## Slide 40
Linear Control
Proposed by Chiu and Jain (1988)
The simplest control strategy
Discussion: values of the parameters?

## Slide 41
State Space of Two Flows
x2
x1
overload
underload
efficiency line: x1+x2=C
fairness line: x1=x2
x(0)

## Slide 42
x0
efficiency
efficiency: distributed linear rule
x0
intersection
x0
congestion
fairness
x0
b=1
a=0

## Slide 43: Implication: Congestion (overload) Case
In order to get closer to efficiency and fairness after each update, decreasing of rate must be multiplicative decrease (MD)
  aD = 0
  bD < 1

## Slide 44
efficiency: distributed linear rule
x0
no-congestion
x0
efficiency
fairness
x0
convergence
x0

## Slide 45: Implication: No Congestion Case
In order to get closer to efficiency and fairness after each update, additive and multiplicative increasing (AMI), i.e.,
  aI > 0, bI > 1
Simply additive increase gives better improvement in fairness (i.e., getting closer to the fairness line)
Multiplicative increase may grow faster

## Slide 46
Intuition: State Trace Analysis of Four Special Cases
 | Additive Decrease | Multiplicative Decrease
Additive Increase | AIAD (bI=bD=1) | AIMD (bI=1, aD=0)
Multiplicative Increase | MIAD (aI=0, bI>1, bD=1) | MIMD (aI=aD=0)
Discussion: state transition trace.

## Slide 47
AIMD: State Transition Trace
x1
x2
x0
fairness line: x1=x2
efficiency line: x1+x2=C
overload
underload

## Slide 48: Intuition: Another Look
Consider the difference or ratio of the rates of two flows
  AIAD
    difference does not change
  MIMD
    ratio does not change
  MIAD
    difference becomes bigger
  AIMD
    difference does not change
Notes: AIAD: difference does not change
MIMD: ratio does not change
MIAD: difference becomes bigger
AIMD: difference does not change

## Slide 49
Outline
Admin and recap
TCP Reliability
Transport congestion control
  what is congestion (cost of congestion)
  basic congestion control alg.
  TCP/reno congestion control

## Slide 50
TCP Congestion Control
Closed-loop, end-to-end, window-based congestion control
Designed by Van Jacobson in late 1980s, based on the AIMD alg. of Dah-Ming Chu and Raj Jain
Worked in a large range of bandwidth values: the bandwidth of the Internet has increased by more than 200,000 times
Many versions
  TCP/Tahoe: this is a less optimized version
  TCP/Reno: many OSs today implement Reno type congestion control
  TCP/Vegas: not currently used
For more details: see TCP/IP illustrated; or read http://lxr.linux.no/source/net/ipv4/tcp_input.c for linux implementation

## Slide 51: Mapping A(M)I-MD to Protocol
Basic questions to look at:
  How to obtain d(t)--the congestion signal?
  What values do we choose for the formula?
  How to map formula to code?
Notes: Implement d(t): loss/delay
Adjust window size
b_D: exponential backoff timeout after window size is 1

## Slide 52: Obtain d(t) Approach 1: End Hosts Consider Loss as Congestion
1
2
3
4
5
6
Packets
Acknowledgements (waiting seq#)
7
2
3
4
4
4
4
Assume loss => cong
Pros and Cons of endhosts using loss as congestion?

## Slide 53: Obtain d(t) Approach 2: Network Feedback (ECN: Explicit Congestion Notification)
Sender 1
Sender 2
Receiver
Network marks ECN Mark (1 bit) on pkt according to local condition, e.g., queue length > K
Receiver bounces marker back to sender in ACK msg
Sender reduces rate if ECN received.
Pros and Cons of ECN?

## Slide 54: Mapping A(M)I-MD to Protocol
Basic questions to look at:
  How to obtain d(t)--the congestion signal?
  What values do we choose for the formula?
  How to map formula to code?
Notes: Implement d(t): loss/delay
Adjust window size
b_D: exponential backoff timeout after window size is 1