## Slide 1: Network Applications: Email, DNS
Qiao Xiang
https://qiaoxiang.me/courses/cnns-xmuf21/index.shtml
9/30/2021
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.

## Slide 2: Outline
Admin. and recap
Application layer overview
Network applications
  Email
  DNS

## Slide 3: Recap: Layering
  Why layering
    reference model
    modularization
  Concepts
    service, interface, and protocol
    physical vs logical communication
  Key design decision
    end-to-end arguments to place functions in layers

## Slide 4: Some Implications of Layered Architecture
A packet as a stack container
Each layer needs multiplexing and demultiplexing to serve layer above
Hn
Hn-1
…
Ln-1
Has a field to indicate which higher layer requires the service
Ln

## Slide 5: Multiplexing/Demultiplexing

## Slide 6: Recap: The Big Picture of the Internet
Hosts and routers:
  ~ 1 bill. hosts
  organized into ~50K networks
  backbone links 100 Gbps
Software:
  datagram switching with virtual circuit support
  layered network architecture
    use end-to-end arguments to determine the services provided by each layer
    the 5-layer hourglass architecture of the Internet
IP
Ethernet
Cable/DSL
Wireless
TCP
UDP
Telnet
Email
FTP
WWW
SSL

## Slide 7
Formats of main protocols
Tip: services map to header fields

## Slide 8: Outline
Admin. and recap
Application layer overview

## Slide 9: Application Layer: Goals
Conceptual + implementation aspects of network application protocols
  client server paradigm
  peer to peer paradigm
  network app. programming
Learn about applications by examining common applications
  smtp/pop
  dns
  http (1, 1.1, /2)
  content distribution
  peer-to-peer

## Slide 10: Network Applications vs. Application-layer Protocols
Network application: communicating, distributed processes
  a process is a program that is running within a host
    a user agent is a process serving as an interface to the user
      web: browser
      streaming audio/video: media player
  processes communicate by an application-layer protocol
    e.g., email, Web
Application-layer protocols
  one “piece” of an app
  define messages exchanged by apps and actions taken
  implementing services by using the service provided by the lower layer, i.e., the transport layer
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 11: App. and Trans.: App. Protocols and their Transport Protocols
Application
e-mail
remote terminal access
Web
file transfer
Internet telephony
remote file server
streaming multimedia
Application
layer protocol
smtp [RFC 821]
telnet [RFC 854]
http [RFC 2068]
ftp [RFC 959]
proprietary
(e.g., Vocaltec)
NFS
proprietary
Underlying
transport protocol
TCP/SSL
TCP
TCP/SSL
TCP
typically UDP
TCP or UDP
typically UDP but moving to http
An application needs to choose the transport protocol

## Slide 12: Client-Server Paradigm
Typical network app has two pieces: client and server
application
transport
network
data link
physical
application
transport
network
data link
physical
Client (C):
initiates contact with server (“speaks first”)
typically requests service from server
for Web, client is implemented in browser; for e-mail, in mail reader
Server (S):
provides requested service to client
e.g., Web server sends requested Web page; mail server delivers e-mail
request
reply

## Slide 13: Client-Server Paradigm: Key Questions
application
transport
network
data link
physical
application
transport
network
data link
physical
request
reply
Key questions to ask about a C-S application
- Is the application extensible?
- Is the application scalable?
- How does the application handle server failures (being robust)?
- How does the application handle security?

## Slide 14: Outline
Admin. and recap
Application layer overview
Network applications
  Email

## Slide 15: Electronic Mail
Still active
  80B emails/day
  3.9B active email boxes
A highly recommended reading: a history of Email development
  linked on the Schedule page

## Slide 16: Recall: SMTP
C: auth login
S: 334 VXNlcm5hbWU6
C: eG11Y25ucw==
S: 334 UGFzc3dvcmQ6
C: MzM0ZjU2MDVkZjE1MDRmOQ==
S: 235 OK Authenticated
C: mail from:xmucnns@sina.com
S: 250 ok
C: rcpt to:qiaoxiang@xmu.edu.cn
S: 250 ok
C: data
S: 354 End data with <CR><LF>.<CR><LF>
C: Date:2021-9-22 12:36
C: From:xmucnns@sina.com
C: To:qiaoxiang@xmu.edu.cn
C: Subject:test smtp
C:
C: Hello, Qiao.
C:
C: .
S: 250 ok queue id 11479549283321
C: quit
S: 221 smtp-97-27.smtpsmail.fmail.bx.sinanode.com
S: Connection closed by foreign host.

## Slide 17: Electronic Mail: Components
Three major components:
User agents
Mail servers
Protocols
  Mail transport protocol
    SMTP
  Mail access protocols
    POP3: Post Office Protocol [RFC 1939]
    IMAP: Internet Mail Access Protocol [RFC 1730]
SMTP
SMTP
SMTP
user mailbox
outgoing
message queue
mail
server
user
agent
user
agent
user
agent
mail
server
user
agent
user
agent
mail
server
user
agent
POP3 or
IMAP SMTP

## Slide 18: Email Transport Architecture
http://www.maawg.org/sites/maawg/files/news/MAAWG_Email_Authentication_Paper_2008-07.pdf

## Slide 19: SMTP: Mail Transport Protocol Messages (Envelop Messages)
C: auth login
S: 334 VXNlcm5hbWU6
C: eG11Y25ucw==
S: 334 UGFzc3dvcmQ6
C: MzM0ZjU2MDVkZjE1MDRmOQ==
S: 235 OK Authenticated
C: mail from:xmucnns@sina.com
S: 250 ok
C: rcpt to:qiaoxiang@xmu.edu.cn
S: 250 ok
C: data
S: 354 End data with <CR><LF>.<CR><LF>
C: Date:2021-9-22 12:36
C: From:xmucnns@sina.com
C: To:qiaoxiang@xmu.edu.cn
C: Subject:test smtp
C:
C: Hello, Qiao.
C:
C: .
S: 250 ok queue id 11479549283321
C: quit
S: 221 smtp-97-27.smtpsmail.fmail.bx.sinanode.com
S: Connection closed by foreign host.
Email text different from SMTP protocol message
%telnet smtp.sina.com 25

## Slide 20: Mail Message Data
SMTP: protocol for exchanging email msgs
RFC 822: standard for text message format:
Header lines, e.g.,
  To:
  From:
  Subject:
Body
  the “message”, ASCII characters only
blank
line
header
body
Benefit of separating protocol and msg: easier extensibility

## Slide 21: Message Format: Multimedia Extensions
MIME: multimedia mail extension, RFC 2045, 2056
Additional lines in msg header declare MIME content type
From: xmucnns@sina.com
To: qiaoxiang@xmu.edu.cn
Subject: Network map.
MIME-Version: 1.0
Content-Type: image/jpeg Content-Transfer-Encoding: base64
base64 encoded data .....
.........................
......base64 encoded data
multimedia data
type, subtype,
parameter declaration
method used
to encode data
MIME version
encoded data
Benefit of MIME type: self describing data type, adding extensibility.

## Slide 22: Multipart Type: How Attachment Works
From: xmucnns@sina.com
To: qiaoxiang@xmu.edu.cn
Subject: Network map.
MIME-Version: 1.0
Content-Type: multipart/mixed; boundary=98766789
--98766789
Content-Transfer-Encoding: quoted-printable
Content-Type: text/plain
Hi,
Attached is network topology map.
--98766789
Content-Transfer-Encoding: base64
Content-Type: image/jpeg
base64 encoded data .....
.........................
......base64 encoded data
--98766789--

## Slide 23: POP3 Protocol: Mail Retrieval
Authorization phase
client commands:
  user: declare username
  pass: password
server responses
  +OK
  -ERR
Transaction phase, client:
list: list message numbers
retr: retrieve message by number
dele: delete
quit
%telnet pop.sina.com 110
S: +OK sina pop3 server ready
C: user xmucnns
S: +OK welcome to sina mail
C: pass 334f5605df1504f9
S: +OK 4 messages (32377 octets)
C: list
S: +OK 4 messages (32377 octets)
S: 1 10410
S: 2 10748
S: 3 7859
S: 4 3360
S: .
C: retr 4
S: +OK 3360 octets
C: dele 2
C: quit
S: +OK
POP3 server signing off
user successfully logged in
Notes: http://www.electrictoolbox.com/article/networking/pop3-commands/

## Slide 24: Exercise
Register an email address at sina.com
Send an email to the registered email address using smtp
Retrieve using pop

## Slide 25: Evaluation of SMTP/POP/IMAP
Key questions to ask about a C-S application
- extensible?
- scalable?
- robust?
- security?
mail
server
user
agent
user
agent
user
agent
mail
server
user
agent
user
agent
mail
server
user
agent
SMTP
SMTP
SMTP
POP3 or
IMAP SMTP

## Slide 26: Email Security: Spam
Spam (Google)
Notes: https://support.google.com/mail/answer/1366858?hl=en
http://www.securelist.com/en/analysis/204792282/Spam_in_January_2013
https://www.trustwave.com/support/labs/spam_statistics.asp
http://en.wikipedia.org/wiki/Bayesian_spam_filtering
http://www.pcworld.com/article/252206/google_explains_gmails_spam_filtering_process.html

## Slide 27: Email Security Issue: Spam
Source: https://www.statista.com/statistics/420400/spam-email-traffic-share-annual/

## Slide 28: Email Security Issue: Spam
Source: https://www.statista.com/statistics/420391/spam-email-traffic-share/

## Slide 29: Discussion: How May One Handle Email Spams?
Notes: https://support.google.com/mail/answer/1366858?hl=en
http://support.simpledns.com/KB/a62/configuring-dns-records-for-domainkeys-dkim.aspx
http://www.slideshare.net/kka7/what-you-need-to-know-about-email-authentication

## Slide 30: Detection Methods Used by GMail
Known phishing scams
Message from unconfirmed sender identity
Message you sent to Spam/similarity to suspicious messages
Administrator-set policies
https://support.google.com/mail/answer/1366858?hl=en
Notes: https://support.google.com/mail/answer/1366858?hl=en
http://support.simpledns.com/KB/a62/configuring-dns-records-for-domainkeys-dkim.aspx

## Slide 31: Email Authentication Approaches
Sender Policy Frame (SPF)
DomainKeys Identified Mail (DKIM) Authenticated Results Chain (ARC)
Notes: https://support.google.com/mail/answer/1366858?hl=en
http://support.simpledns.com/KB/a62/configuring-dns-records-for-domainkeys-dkim.aspx
https://dmarc.org/presentations/ARC-Overview-2016Q3-v01.pdf

## Slide 32: Sender Policy Framework (SPF RFC7208)
MUA
MTA
Border Outbound MTA m
Border Inbound MTA
MUA
smtp/submission
smtp
smtp
pop/imap
neighbor MTA
validating MTA
Is my neighbor m a permitted sender for the domain?
https://tools.ietf.org/html/rfc7208
Notes: https://support.google.com/mail/answer/1366858?hl=en
http://support.simpledns.com/KB/a62/configuring-dns-records-for-domainkeys-dkim.aspx

## Slide 33: Key Question for SPF?
How does SPF know if its neighbor MTA is a permitted sender of the domain?
Notes: http://support.simpledns.com/KB/a62/configuring-dns-records-for-domainkeys-dkim.aspx
<selector>._domainkey.example.com
  dig txt <selector>._domainkey.<domain> +short

## Slide 34: DomainKeys Identified Mail (DKIM; RFC 5585)
A domain-level digital signature authentication framework for email, using public key crypto
  E.g., mail.sina.com signs that the message is sent by mail.sina server
Basic idea of public key signature
  Owner has both public and private keys
  Owner uses private key to sign a message to generate a signature
  Others with public key can verify signature
  Assumption: difficult to get private key even w/ public key distributed
Notes: mailing lists or account forwarding
https://blog.returnpath.com/how-to-explain-authenticated-received-chain-arc-in-plain-english-2/
https://support.google.com/mail/answer/1366858?hl=en
http://support.simpledns.com/KB/a62/configuring-dns-records-for-domainkeys-dkim.aspx

## Slide 35: DomainKeys Identified Mail (DKIM)
MUA
Signing MTA
MTA
VerifyingMTA
MUA
smtp/submission
smtp
smtp
pop/imap
Is the message signed by the private key of the signing domain?
Notes: https://support.google.com/mail/answer/1366858?hl=en
http://support.simpledns.com/KB/a62/configuring-dns-records-for-domainkeys-dkim.aspx

## Slide 36: Example: RSA
1. Choose two large prime numbers p, q.
(e.g., 1024 bits each)
2. Compute n = pq, z = (p-1)(q-1)
3. Choose e (with e < n) that has no common factors
with z. (e, z are “relatively prime”).
4. Choose d such that ed-1 is exactly divisible by z.
(in other words: ed mod z = 1 ).
5. Public key is (n,e). Private key is (n,d).

## Slide 37: RSA: Signing/Verification
0. Given (n,e) and (n,d) as computed above
1. To sign message, m, compute h = hash(m), then sign with private key
s = h mod n
d
(i.e., remainder when h is divided by n)
d
2. To verify signature s, compute
h’ = s mod n
e
(i.e., remainder when s is divided by n)
e
h = (h mod n)
d
mod n
e
Magic
happens!
The magic is a simple application of Euler’s generalization of
Fermat’s little theorem

## Slide 38: Key Question about DKIM?
How does DKIM retrieve the public key of the author domain?
Notes: http://support.simpledns.com/KB/a62/configuring-dns-records-for-domainkeys-dkim.aspx
<selector>._domainkey.example.com
  dig txt <selector>._domainkey.<domain> +short

## Slide 39: Summary: Some Key Remaining Issues about Email
Basic: How to find the email server of a domain?
Scalability/robustness: how to find multiple servers for the email domain?
Security
  SPF: How does SPF know if its neighbor MTA is a permitted sender of the domain?
  DKIM: How does DKIM retrieve the public key of the author domain?

## Slide 40: Scalability/Robustness
Both scalability and robustness require that multiple email servers serve the same email address
client
need an email server’s IP address
mail
server
mail
server
mail
server
sina.com
sina.com
sina.com
130.132.50.7
130.132.50.8
130.132.50.9
mapping

## Slide 41: Mapping Functions Design Alternatives
mapping
name (e.g., sina.com)
1 IP
mapping
multiple IPs
mapping
multiple IPs
name (e.g., sina.com)

## Slide 42: Mapping Functions Design Alternatives
load balancer (routing)
switch
mapping
name (e.g., sina.com)
1 IP
mapping
name (e.g., sina.com)
1 IP
1 IP

## Slide 43: Outline
Admin. and recap
Layered network architecture
Application layer overview
Network applications
  Email
  DNS

## Slide 44: DNS: Domain Name System
Function
  map between (domain name, service) to value, e.g.,
    (xmu.edu.cn, addr) -> 210.34.0.35
    (xmu.edu.cn, email) -> cmsn1.xmu.edu.cn
routers
DNS
Hostname, Service
Address
servers
clients
Notes: Why name: easy to remember, one-level of indirection

## Slide 45: DNS Records
DNS: stores resource records (RR)
Type=NS
  name is domain (e.g. xmu.edu.cn)
  value is the name of the authoritative name server for this domain
RR format: (name, type, value, ttl)
Type=A
  name is hostname
  value is IP address
Type=CNAME
  name is an alias of a “canonical” (real) name
  value is canonical name
Type=MX
  value is hostname of mail server associated with name
Type=SRV
  general extension for services
Type=TXT
  general txt
http://www.iana.org/assignments/dns-parameters/dns-parameters.xhtml
Type=PTR
  a pointer to another name

## Slide 46: Discussion
Can DNS handle multiple values for the same (name, service)?

## Slide 47: Try DNS: Examples
dig <name> <type>
  Try xmu.edu.cn / others and various types
dig <domain> txt to retrieve spf
http://www.zytrax.com/books/dns/ch9/spf.html

## Slide 48: Observations
MX can return multiple servers
DNS may rotate the servers in answer
Address can also return multiple addresses
SPF is encoded as the txt type

## Slide 49: DKIM Example
Send email from hotmail and check message
Notes: https://support.google.com/mail/answer/1366858?hl=en
http://support.simpledns.com/KB/a62/configuring-dns-records-for-domainkeys-dkim.aspx
Try TXT record for gmail.com dig txt gmail.com

## Slide 50: DKIM Example
DKIM / ARC: Msg: ARC-Message-Signature: i=1; a=rsa-sha256; c=relaxed/relaxed; d=microsoft.com; s=arcselector9901; h=From:Date:Subject:Message-ID:Content-Type:MIME-Version; bh=bO91TxHI+4MjgAusrfg0EWGiDmvQ5hZRZ/aqb1MKLY8=; …
DKIM-Signature: v=1; a=rsa-sha256; c=relaxed/relaxed;
d=hotmail.com; s=selector1; h=From:Date:Subject:Message-
ID:Content-Type:MIME-Version:X-MS-Exchange-
SenderADCheck;…
Query: dig arcselector9901._domainkey.microsoft.com txt
DKIM introduces a session key to allow multiple public keys
  <session>._domainkey.<domain>

## Slide 51
DNS Design: Dummy Design
DNS itself can be considered as a client-server system as well
How about a dummy design: introducing one super Internet DNS server?
THE DNS server of the Internet
register <name>
resolve <name>
OK/used already
IP address

## Slide 52: Problems of a Single DNS Server
Scalability and robustness bottleneck
Administrative bottleneck

## Slide 53: DNS: Distributed Management of the Domain Name Space
A distributed database managed by authoritative name servers
  divided into zones, where each zone is a sub-tree of the global tree
  each zone has its own authoritative name servers
  an authoritative name server of a zone may delegate a subset (i.e. a sub-tree) of its zone to another name server
called a zone
cn
xmu
pku
mail
cwc

## Slide 54: Email Architecture + DNS
mail
server
user
agent
user
agent
user
agent
mail
server
user
agent
user
agent
mail
server
user
agent
SMTP
SMTP
SMTP
POP3 or
IMAP SMTP
DNS

## Slide 55
Root Zone and Root Servers
The root zone is managed by the root name servers
  13 root name servers worldwide
See http://root-servers.org/ for more details

## Slide 56
Linking the Name Servers
Each name server knows the addresses of the root servers
Each name server knows the addresses of its immediate children (i.e., those it delegates)
Top level domain (TLD)
Q: how to query a hierarchy?

## Slide 57
DNS Message Flow: Two Types of Queries
Recursive query:
The contacted name server resolves the name completely
Iterated query:
Contacted server replies with name of server to contact
  “I don’t know this name, but ask this server”

## Slide 58
Two Extreme DNS Message Flows
client
informatics.xmu.edu.cn
root name server
1
2
3
authoritative name server
5
6
TLD name server
4
client
informatics.xmu.edu.cn
root name server
1
6
2
authoritative name server
4
3
TLD name server
5
Q: Issues of the two approaches?
Iterative query
Recursive query
A: ALL the load has to go through the root server!

## Slide 59
Typical DNS Message Flow: The Hybrid Case
requesting host
cyndra.cs.yale.edu
gaia.cs.umass.edu
root name server
1
2
3
4
authoritative name server
dns.cs.umass.edu
5
6
TLD name server
7
8
iterated query
local name server
130.132.1.9
Host knows only local name server
Local name server is learned from DHCP, or configured, e.g. /etc/resolv.conf
Local DNS server helps clients resolve DNS names

## Slide 60
Typical DNS Message Flow: The Hybrid Case
requesting host
harvard.edu
gaia.cs.umass.edu
root name server
1
2
3
4
authoritative name server
dns.cs.umass.edu
5
6
TLD name server
7
8
iterated query
local name server
Host knows only local name server
Local name server is learned from DHCP, or configured, e.g. /etc/resolv.conf
Local DNS server helps clients resolve DNS names
Benefits of local name servers (often called resolvers)
  simplifies client
  caches/reuses results

## Slide 61: Outline
Admin. and recap
Layered network architecture
Application layer overview
Network applications
  Email
  DNS
    High-level design
    Details

## Slide 62
IP
Ethernet
Cable/DSL
Wireless
TCP
UDP
DNS
IP
Ethernet
Cable/DSL
Wireless
TCP
UDP
DNS
DNS Message Format?
Basic encoding decisions: UDP/TCP, how to encode domain name, how to encode answers…
62
Notes: Basic questions: how to encode domain name; how to do compression…