## Slide 1: Layered Network Architecture; Network Applications: Overview, EMail
Qiao Xiang
https://qiaoxiang.me/courses/cnns-xmuf21/index.shtml
9/28/2021
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.

## Slide 2: Outline
Admin. and recap
Layered network architecture
Application layer overview
Network applications
  Email

## Slide 3: Admin
Questions on Assignment One

## Slide 4
Recap: Summary of the Taxonomy of Communication Networks
circuit-switched network
communication network
switched network
broadcast communication
packet-switched network
datagram network
virtual circuit network

## Slide 5: Recap: Circuit Switching vs. Packet Switching
 | circuit switching | packet switching
resource usage | use a single partition bandwidth | use whole link bandwidth
reservation/setup | need reservation (setup delay) | no reservation
resource contention | busy signal (session loss) | congestion (long delay and packet losses)
charging | time | packet
header | no per-pkt header | per packet header
fast path processing | fast | per packet processing

## Slide 6: Recap: Queueing Theory
Model system state
Introduce state transition diagram
Focus on equilibrium: state trend neither growing nor shrinking

## Slide 7: Recap: Queueing Theory Analysis of Circuit-Switching
0
1
k
N
system state: # of busy lines
p0
p1
pk
k+1
pk+1
pN

## Slide 8: Equilibrium = Time Reversibility [Frank Kelly]
Statistically cannot distinguish
time
state
k
k+1
=
=
=
Play the sequence backwards

## Slide 9: Recap: Queueing Theory Analysis of Circuit-Switching
0
1
k
N
system state: # of busy lines
at equilibrium (time reversibility) in one unit time: #(transitions k  k+1) = #(transitions k+1  k)
p0
p1
pk
k+1
pk+1

(k+1)
pN

## Slide 10: Recap: Queueing Theory Analysis of Packet Switching
0
1
k
N
system state: #packets in queue
at equilibrium (time reversibility) in one unit time: #(transitions k  k+1) = #(transitions k+1  k)
p0
p1
pk
k+1
pk+1



## Slide 11: Recap: Analysis of Delay
Average queueing delay:
Transmission delay:
Queueing + transmission:
0
1
k
k+1



## Slide 12
Recap: Analysis of Delay
For a demo of M/M/1, see: http://www.dcs.ed.ac.uk/home/jeh/Simjava/queueing/mm1_q/mm1_q.html

## Slide 13: Recap: Statistical Multiplexing
no reservation: all arrivals into the single link, the queueing delay + transmission delay:
reservation: each flow uses its own reserved (sub)link with rate /n, the queueing delay + transmission delay:
A simple model to compare bandwidth efficiency of
- reservation/dedication (aka circuit-switching) vs
- no reservation (aka packet switching) setup
- a single bottleneck link with
service rate
- flows; each flow has an arrival rate of
For each flow i:

## Slide 14: Summary of Progress
We have seen the hardware infrastructure, the basic communication scheme, a next key question is how to develop the software system.

## Slide 15
Outline
Admin. and recap
Layered network architecture
  what is layering?
  why layering?
  how to determine the layers?
  ISO/OSI layering and Internet layering

## Slide 16
A technique to organize a networked system into a succession of logically distinct entities, such that the service provided by one entity is solely based on the service provided by the previous (lower level) entity.
What is Layering?
Application
Transport
Network
Datalink
Physical
Application
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Physical medium

## Slide 17
Outline
Admin. and recap
Layered network architecture
  what is layering?
  why layering?

## Slide 18
Why Layering?
Dealing with complex systems: explicit structure allows identification of the relationship among a complex system’s pieces
  layered reference model for discussion
Networks are complex !
many “pieces”:
  hardware
    hosts
    routers
    links of various media
  software
    applications
    infrastructure
Modularization eases maintenance, updating of system:
  change of implementation of a layer’s service transparent to rest of system, e.g., changes in routing protocol doesn’t affect rest of system

## Slide 19: An Example: No Layering
No layering: each new application has to be re-implemented for every network technology !
Telnet
FTP
Wireless
Ether-net
Fiber
optic
Application
Transmission
Media
HTTP

## Slide 20: An Example: Benefit of Layering
Introducing an intermediate layer provides a common abstraction for network technologies
HTTP
Telnet
FTP
Wireless
Ethernet
Fiber
optic
Application
Transmission
Media
Transport
& Network

## Slide 21
ISO/OSI Concepts
ISO – International Standard Organization
OSI – Open System Interconnection
Service – says what a layer does
Interface – says how to access the service
Protocol – specifies how the service is implemented
  a set of rules and formats that govern the communications between two or more peers

## Slide 22: An Example of Layering

## Slide 23: An Example of Layering

## Slide 24: Layering -> Logical Communication
E.g.: application
provide services to users
application protocol:
  send messages to peer
  for example, HELO, MAIL FROM, RCPT TO are messages between two SMTP peers

## Slide 25
Layering: Logical Communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data
E.g.: transport
Trans. msg for app
Transport protocol
  add control info to form “segment”
  send segment to peer
  wait for peer to ack receipt; if no ack, retransmit
data
transport
transport
ack

## Slide 26
Layering: Physical Communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data

## Slide 27
Protocol Layering and Meta Data
Each layer takes data from above
adds header (meta) information to its peer to create new data unit
passes new data unit to layer below

## Slide 28: Packet as a Stack in a Layered Architecture
Application
Transport
Network
Datalink
Physical
Application
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Physical medium

## Slide 29: Some Implications of Layered Architecture
A packet as a stack container
Each layer needs multiplexing and demultiplexing to serve layer above
Hn
Hn-1
…
Ln-1
Has a field to indicate which higher layer requires the service
Ln

## Slide 30
Key design issue:
How do you divide functionalities among the layers?

## Slide 31
Admin. and recap
Layered network architecture
  what is layering?
  why layering?
  how to determine the layers?
Outline

## Slide 32
The End-to-End Arguments
The function in question can completely and correctly be implemented only with the knowledge and help of the application standing at the endpoints of the communication systems. Therefore, providing that questioned function as a feature of the communications systems itself is not possible.
J. Saltzer, D. Reed, and D. Clark, 1984

## Slide 33
What does the End-to-End Arguments Mean?
The application knows the requirements best, place functionalities as high in the layer as possible
Think twice before implementing a functionality at a lower layer, even when you believe it will be useful to an application

## Slide 34
Example: Where to Provide Reliability ?
Solution 1: the network (lower layer L1) provides reliability, i.e., each hop provides reliability
Solution 2: the end host (higher layer L2) provides reliability, i.e., end-to-end check and retry
L1
L2
L1
S
R
L1
L2
A

## Slide 35
What are Reasons for Implementing Reliability at Higher Layer ?
The lower layer cannot completely provide the functionality
  the receiver has to do the check anyway !
Implementing it at lower layer increases complexity, cost and overhead at lower layer
  shared by all upper layer applications  everyone pays for it, even if you do not need it
The upper layer
  knows the requirements better and thus may choose a better approach to implement it
L1
L2
L1
S
R
L1
L2
A
Notes: First point: L1 may first ack and then crash; then the function fails; if L2 crash; the application crashes also->fate sharing

## Slide 36
Are There Reasons Implementing Reliability at Lower Layer ?
Improve performance, e.g., if high cost/delay/… on a local link
  improves efficiency
  reduces delay
Share common code, e.g., reliability is required by multiple applications
L1
L2
L1
S
R
L1
L2
A
Notes: S to A: San francisco to Yale router
A to R: Yale router to a wireless laptop (e.g., 10% success rate)

## Slide 37: Summary: End-to-End Arguments
If a higher layer can do it, don’t do it at a lower layer -- the higher the layer, the more it knows about the best what it needs
Add functionality in lower layers iff it
    (1) is used by and improves performance of a large number of (current and potential future) applications,
    (2) does not hurt (too much) other applications, and
    (3) does not increase (too much) complexity/overhead
Practical tradeoff, e.g.,
  allow multiple interfaces at a lower layer (one provides the function; one does not)
Notes: Issue: does not reduce complexity/cost
upper layer needs to be developed for all interfaces

## Slide 38
We used reliability as an example
Assume two layers (L1: network; L2: end-to-end). Where may you implement the following functions?
  security (privacy of traffic)
  quality of service (e.g., delay/bandwidth guarantee)
  congestion control (e.g., not to overwhelm network links or receiver)
Examples
L1
L2
L1
S
R
L1
L2
A

## Slide 39: Example
Consider the presence service in a social networking system: shows which contacts are online (e.g., skype)
  implementing by end user’s host app or through a third party service?
L2
L1
A
B
L2

## Slide 40: Challenges
Challenges to build a good (networking) system: find the right balance between:
reuse, interoperability, implementation effort
(apply layering concepts)
end-to-end arguments
performance
No universal answer: the answer depends on the goals and assumptions!

## Slide 41: Discussion: Limitations of Layered Architecture

## Slide 42: Outline
Admin. and recap
Layered network architecture
  what is layering?
  why layering?
  how to determine the layers?
  ISO/OSI layering and Internet layering

## Slide 43
ISO/OSI Reference Model
Seven layers
  highest four layers are implemented in host
Application
Presentation
Session
Transport
Network
Datalink
Physical
Application
Presentation
Session
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Physical medium

## Slide 44
Internet Layering
Five layers
  highest two layers are implemented in host
Application
Transport
Network
Datalink
Physical
Application
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Physical medium

## Slide 45
Internet Protocol Layers
Five layers
  Application: applications
    ftp, smtp, http, p2p, IP telephony, blockchain, MapReduce, …
  Transport: host-host data transfer
    tcp (reliable), udp (not reliable)
  Network: routing of datagram from source to destination
    ipv4, ipv6
  Link: data transfer between neighboring network elements
    ethernet, 802.11, cable, DSL, …
  Physical: bits “on the wire”
    cable, wireless, optical fiber
application
transport
network
link
physical

## Slide 46
The Hourglass Architecture of the Internet
network
infrastructure
end users
IP4
Ethernet
Cable/DSL
Wireless
TCP
UDP
Telnet
Email
FTP
WWW
Notes: How about move the line to on top of TCP/UDP?

## Slide 47
Link Layer (Ethernet)
Services (to network layer)
  multiplexing/demultiplexing
    - from/to the network layer
  error detection
  multiple access control
    arbitrate access to shared medium
Interface
  send frames to a directly reachable peer
IP4/6
Ethernet
Cable/DSL
Wireless
TCP
UDP
Telnet
Email
FTP
WWW

## Slide 48
Link Layer: Protocol Header (Ethernet)
IP4/6
Ethernet
Cable/DSL
Wireless
TCP
UDP
Telnet
Email
FTP
WWW
IP4/6
Ethernet
Cable/DSL
Wireless
TCP
UDP
Telnet
Email
FTP
WWW
IP4
link
IP6
IP4
link
IP6
access control
error
detection
multiplexing
/demultiplexing

## Slide 49
Network Layer: IP
Services (to transport layer)
  multiplexing/demultiplexing from/to the transport
  fragmentation and reassembling: partition a fragment into smaller packets
    - removed in IPv6
  error detection
  routing: best-effort to send packets from source to destination
  certain QoS/CoS
  does not provide reliability or reservation
Interface:
  send a packet to a (transport-layer) peer at a specified global destination, with certain QoS/CoS
IP
Ethernet
Cable/DSL
Wireless
TCP
UDP
SSL
Telnet
Email
FTP
WWW

## Slide 50
IP
Ethernet
Cable/DSL
Wireless
TCP
UDP
SSL
Telnet
Email
FTP
WWW
IP
Ethernet
Cable/DSL
Wireless
TCP
UDP
SSL
Telnet
Email
FTP
WWW
Network Layer: IPv4 Header
multiplexing
/demultiplexing
fragmentation / reassembling
error
detection
routing
QoS/CoS

## Slide 51
Transport Layer: UDP
A connectionless service
Does not provide: connection setup, reliability, flow control, congestion control, timing, or bandwidth guarantee
  why is there a UDP?
IP
Ethernet
Cable/DSL
Wireless
TCP
UDP
Telnet
Email
FTP
WWW

## Slide 52: Transport Services and APIs
Multiple services and APIs proposed in history
  XTI (X/Open Transport Interface), a slight modification of the Transport Layer Interface (TLI) developed by AT&T.
Commonly used transport-layer service model and API: Socket
  sometimes called "Berkeley sockets" acknowledging their heritage from Berkeley Unix
  a socket has a transport-layer local port number
    e.g., email (SMTP) port number 25, web port number 80
  Application can send data into socket, read data out of socket
  an application process binds to a socket (-a all; -u udp; -n number)
    %netstat -aun
Notes: http://www.techrepublic.com/blog/security/list-open-ports-and-listening-services/
lsof –i -n

## Slide 53: Socket Service Model and API
buffers,
states
buffers,
states
transport
protocol

## Slide 54: Multiplexing/Demultiplexing

## Slide 55
Transport Layer: UDP Header
IP
Ethernet
Cable/DSL
Wireless
TCP
UDP
Telnet
Email
FTP
WWW
IP
Ethernet
FDDI
Wireless
UDP
TCP
Telnet
Email
FTP
WWW
multiplexing
/demultiplexing
error
detection

## Slide 56
Transport Layer: TCP
Services
  multiplexing/demultiplexing
  reliable transport
    between sending and receiving processes
    setup required between sender and receiver: a connection-oriented service
  flow control: sender won’t overwhelm receiver
  congestion control: throttle sender when network overloaded
  error detection
  does not provide timing, minimum bandwidth guarantees
Interface:
  send a packet to a (app-layer) peer
IP
Ethernet
FDDI
Wireless
TCP
UDP
Telnet
Email
FTP
WWW

## Slide 57
Transport Layer: TCP Header
IP
Ethernet
Cable/DSL
Wireless
UDP
TCP
Telnet
Email
FTP
WWW
IP
Ethernet
FDDI
Wireless
TCP
UDP
Telnet
Email
FTP
WWW
multiplexing
/demultiplexing
Reliable
transport
flow control
congestion
control
error
detection

## Slide 58: Secure Socket Layer Architecture
HTTP
POP3

## Slide 59: SSL Record-Layer Packet Format
20: change_cipher
21: alert
22: handshake
23: application

## Slide 60: Summary: The Big Picture of the Internet
Hosts and routers:
  ~ 1 bil. hosts
  autonomous systems organized roughly hierarchical
  backbone links at 100 Gbps
Software:
  datagram switching with virtual circuit support at backbone
  layered network architecture
    use end-to-end arguments to determine the services provided by each layer
  the hourglass architecture of the Internet
IP4/6
Ethernet
Cable/DSL
Wireless
TCP
UDP
Telnet
Email
FTP
WWW
SSL

## Slide 61
Protocol Formats

## Slide 62: DEMO: SMTP
C: auth login
S: 334 VXNlcm5hbWU6
C: eG11Y25ucw==
S: 334 UGFzc3dvcmQ6
C: MzM0ZjU2MDVkZjE1MDRmOQ==
S: 235 OK Authenticated
C: mail from:xmucnns@sina.com
S: 250 ok
C: rcpt to:qiaoxiang@xmu.edu.cn
S: 250 ok
C: data
S: 354 End data with <CR><LF>.<CR><LF>
C: Date:2021-9-22 12:36
C: From:xmucnns@sina.com
C: To:qiaoxiang@xmu.edu.cn
C: Subject:test smtp
C:
C: Hello, Qiao.
C:
C: .
S: 250 ok queue id 11479549283321
C: quit
S: 221 smtp-97-27.smtpsmail.fmail.bx.sinanode.com
S: Connection closed by foreign host.

## Slide 63: Backup Slides

## Slide 64: The Design Philosophy of the DARPA Internet

## Slide 65: Goals
Survivability in the face of failure
Support multiple types of services
Accommodate a variety of networks
Permit distributed management of resources
Be cost effective
Permit host attachment with a low level of effort
Be accountable
. Connect different networks

## Slide 66: Survivability in the Face of Failure: Questions
What does the goal mean?
Why is the goal important?
How does the Internet achieve this goal?
Does the Internet achieve this goal (or in what degree does the Internet achieve this goal)?

## Slide 67
Survivability in the Face of Failure
Continue to operate even in the presence of network failures (e.g., link and router failures)
  as long as the network is not partitioned, two endpoints should be able to communicate…moreover, any other failure (excepting network partition) should be transparent to endpoints
Decision: maintain state only at end-points (fate-sharing)
  eliminate the problem of handling state inconsistency and performing state restoration when router fails
Internet: stateless network architecture

## Slide 68: Support Multiple Types of Service: Questions
What does this goal mean?
Why is the goal important?
How does the Internet achieve this goal?
Does the Internet achieve this goal (or in what degree does the Internet achieve this goal)?

## Slide 69: Support Multiple Types of Service
Add UDP to TCP to better support other types of applications
  e.g., “real-time” applications
This was arguably the main reason for separating TCP and IP
Provide datagram abstraction: lower common denominator on which other services can be built: everything over IP
  service differentiation was considered (remember ToS?), but this has never happened on the large scale (Why?)

## Slide 70: Support a Variety of Networks: Questions
What does the goal mean?
Why is this goal important?
How does the Internet achieve this goal?
Does the Internet achieve this goal (or in what degree does the Internet achieve this goal)?

## Slide 71: Support a Variety of Networks
Very successful
  because the minimalist service; it requires from underlying network only to deliver a packet with a “reasonable” probability of success
…does not require:
  reliability
  in-order delivery
The mantra: IP over everything
  Then: ARPANET, X.25, DARPA satellite network..
  Now: ATM, SONET, WDM…

## Slide 72: Other Goals
Permit distributed management of resources
Be cost effective
Permit host attachment with a low level of effort
Be accountable