## Slide 1: Network Transport Layer: Transport Reliability: Sliding Windows; Connection Management; TCP
Qiao Xiang
https://qiaoxiang.me/courses/cnns-xmuf21/index.shtml
11/11/2021
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.

## Slide 2: Recap: Reliable Data Transfer Context
send
side
receive
side
rdt_send(): called from above, (e.g., by app.)
udt_send(): called by rdt,
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called from below; when packet arrives on rcv-side of channel
deliver_data(): called by rdt to deliver data to upper

## Slide 3: Recap: rdt2.0: Reliability allowing only Data Msg Corruption
Wait for data
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for data
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
sender
receiver
Wait for ACK or NAK
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
L
3

## Slide 4
Recap: Rdt2.0 Analysis
sender
data (n)
receiver
data (n)
ACK
data (n+1)
waiting for N/ACK
waiting for data
NACK
Execution traces of rdt2.0: {data^ NACK}* data deliver ACK

## Slide 5: Recap: rdt2.1b: Reliability allowing Data/Control Msg Corruption
sender
receiver
Guess garbled feedback as NAK
Fix wrong guess by checking seq#
5

## Slide 6
Protocol Analysis using (Generic) Execution Traces Technique
Issue: how to systematically enumerate all potential execution traces to understand and verify correctness
A systematic approach to enumerating exec. traces is to compute joint sender/receiver/channels state machine
wn rn - -
sender state: waiting for n
snd->rcv channel state
receiver state: waiting for n
rcv>snd channel state
sn rn dn -
snd dn
sn rn+1 - ACK
rcv dn del
rcv d^n
sn rn - NAK
…
…
6
Notes: {data(n)^ NACK|NACK^}* data(n) deliver
ACK^ data(n)
ACK^ data(n)^ XXXX

## Slide 7
Recap: Protocol Analysis using (Generic) Execution Traces Technique
wn rn - -
sn rn dn -
sn rn+1 - ACK
sn rn - NAK
sn rn+1 - NAK
sn rn+1 dn -
Wn+1 rn+1 - -
s dn
r dn
deliv
s ACK
r ACK
r NAK| r NAK^ s dn
r dn^ s NAK
r dn
s ACK
r NAK| r NAK^
s dn
r dn^
s NAK
r ACK^
s dn
Execution traces of rdt2.1b are all that can be generated by the finite state machine above.
7
Notes: {data(n)^ NACK|NACK^}* data(n) deliver
ACK^ data(n)
ACK^ data(n)^ XXXX

## Slide 8
Recap: Protocol Analysis using State Invariants
s0
sender
s1
s2
receiver
w0
w1
w2
w3
w3
first
time
rcvs 0
first
time
rcvs
ack 0
w0
w1
w2
W1: wait for data with seq. 1
S1: sending data with seq. 1
State invariant:
- When receiver’s state is waiting for seq #n, sender’s state can be sending either seq#n-1or seq#n, and only either #n or #n-1 packets can arrive

## Slide 9: rdt2.1c: Sender, Handles Garbled ACK/NAKs: Using 1 bit (Alternating-Bit Protocol)
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
Wait for
call 1 from above
Wait for ACK or NAK 1
L
L

## Slide 10: rdt2.1c: Receiver, Handles Garbled ACK/NAKs: Using 1 bit
Wait for
0 from below
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq0(rcvpkt)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
Wait for
1 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq1(rcvpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)

## Slide 11: rdt2.1c: Summary
Sender:
state must “remember” whether “current” pkt has 0 or 1 seq. #
Receiver:
must check if received packet is duplicate
  state indicates whether 0 or 1 is expected pkt seq #

## Slide 12: rdt2.2: a NAK-free protocol
Same functionality as rdt2.1c, using ACKs only
Instead of NAK, receiver sends ACK for last pkt received OK
  receiver must explicitly include seq # of pkt being ACKed
Duplicate ACK at sender results in same action as NAK: retransmit current pkt

## Slide 13: rdt2.2: Sender, Receiver Fragments
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
Wait for ACK 0
sender FSM
fragment
Wait for
0 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK,0, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
(corrupt(rcvpkt) ||
has_seq1(rcvpkt))
sndpkt= make_pkt(ACK,1, chksum)
udt_send(sndpkt)
receiver FSM
fragment
L

## Slide 14
Outline
Admin and review
Reliable data transfer
  perfect channel
  channel with bit errors
  channel with bit errors and losses

## Slide 15: rdt3.0: Channels with Errors and Loss
New assumption: underlying channel can also lose packets (data or ACKs)
  checksum, seq. #, ACKs, retransmissions will be of help, but not enough
Q: Does rdt2.2 work under losses?
Approach: sender waits “reasonable” amount of time for ACK
requires countdown timer
retransmits if no ACK received in this time
if pkt (or ACK) just delayed (not lost):
  retransmission will be duplicate, but use of seq. #’s already handles this
  receiver must specify seq # of pkt being ACKed

## Slide 16: rdt3.0 Sender
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for ACK0
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
Wait for
call 1 from above
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,0) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
stop_timer
timeout
udt_send(sndpkt)
start_timer
udt_send(sndpkt)
start_timer
timeout
rdt_rcv(rcvpkt)
Wait for
call 0 from above
Wait for ACK1
L
rdt_rcv(rcvpkt)
L
L
L
udt_send(sndpkt)

## Slide 17: rdt3.0 in Action

## Slide 18: rdt3.0 in Action
Question to think about: How to determine a good timeout value?
Home exercise: What are execution traces of rdt3.0? What are some state invariants of rdt3.0?

## Slide 19: rdt3.0: Protocol Analysis using State Invariants
sender
data 0 (n-1)
receiver
data 0 (n-1)
ACK for 0 (n-1)
data 1 (n)
waiting for 0 (n-1)
sending 0 (n-1)
waiting for 1
(n)
sending 1 (n)
waiting for 0 (n+1)
ACK for 0 (n-1)
State consistency:
When receiver’s state is waiting n, the state of the sender is either sending for n-1 or sending for n
When sender’s state is sending for n, receiver’s state is waiting for n or n + 1

## Slide 20: rdt3.0: Stop-and-Wait Performance
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
  What is Usender: utilization – fraction of time link busy sending?
Assume: 1 Gbps link, 15 ms e-e prop. delay, 1KB packet
20

## Slide 21: Performance of rdt3.0
rdt3.0 works, but performance stinks
Example: 1 Gbps link, 15 ms e-e prop. delay, 1KB packet:
T
transmit
=
8kb/pkt
10**9 b/sec
= 8 microsec
  1KB pkt every 30 msec -> 33kB/sec thruput over 1 Gbps link
  network protocol limits use of physical resources !
L (packet length in bits)
R (transmission rate, bps)
=

## Slide 22
A Summary of Questions
How to improve the performance of rdt3.0?
What if there are reordering and duplication?
How to determine the “right” timeout value?
22

## Slide 23: Sliding Window Protocols: Pipelining
Pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged pkts
  range of sequence numbers must be increased
  buffering at sender and/or receiver
23
Notes: Two generic forms of pipelined protocols: go-Back-N, selective repeat

## Slide 24
Pipelining: Increased Utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
increase utilization
by a factor of 3!
Question: a rule-of-thumb window size?
24

## Slide 25: Realizing Sliding Window: Go-Back-n
Sender:
k-bit seq # in pkt header
“window” of up to W, consecutive unack’ed pkts allowed
ACK(n): ACKs all pkts up to, including seq # n - “cumulative ACK”
  note: ACK(n) could mean two things: I have received upto and include n, or I am waiting for n
timer for the packet at base
timeout(n): retransmit pkt n and all higher seq # pkts in window
W
25

## Slide 26
GBN: Sender FSM
Wait
start_timer
udt_send(sndpkt[base])
udt_send(sndpkt[base+1])
…
udt_send(sndpkt[nextseqnum-1])
timeout
rdt_send(data)
if (nextseqnum < base+W) {
sndpkt[nextseqnum] = make_pkt(nextseqnum,data,chksum)
udt_send(sndpkt[nextseqnum])
if (base == nextseqnum) start_timer
nextseqnum++
} else
block sender
if (new packets ACKed) {
advance base;
if (more packets waiting) send more packets
}
if (base == nextseqnum)
stop_timer
else
start_timer for the packet at new base
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
base=1
nextseqnum=1
rdt_rcv(rcvpkt)
&& corrupt(rcvpkt)
L
26

## Slide 27
GBN: Receiver FSM
Only state: expectedseqnum
out-of-order pkt:
  discard (don’t buffer) -> no receiver buffering!
  re-ACK pkt with highest in-order seq #
  may generate duplicate ACKs
Wait
udt_send(sndpkt)
default
rdt_rcv(rcvpkt)
&& notcurrupt(rcvpkt)
&& hasseqnum(rcvpkt,expectedseqnum)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(expectedseqnum,ACK,chksum)
udt_send(sndpkt)
expectedseqnum++
expectedseqnum=1
sndpkt =
make_pkt(expectedseqnum,ACK,chksum)
L
27

## Slide 28: GBN in Action
window
size = 4
28

## Slide 29: Analysis: Efficiency of Go-Back-n
Assume window size W
Assume each packet is lost with probability p
On average, how many packets do we send for each data packet received?
29

## Slide 30: Selective Repeat
Sender window
  Window size W: W consecutive unACKed seq #’s
Receiver individually acknowledges correctly received pkts
  buffers out-of-order pkts, for eventual in-order delivery to upper layer
  ACK(n) means received packet with seq# n only
  buffer size at receiver: window size
Sender only resends pkts for which ACK not received
  sender timer for each unACKed pkt
30

## Slide 31: Selective Repeat: Sender, Receiver Windows
W
W
31

## Slide 32: Selective Repeat
data from above :
unACKed packets is less than window size W, send; otherwise block app.
timeout(n):
resend pkt n, restart timer
ACK(n) in [sendbase,sendbase+W-1]:
mark pkt n as received
update sendbase to the first packet unACKed
sender
pkt n in [rcvbase, rcvbase+W-1]
send ACK(n)
if (out-of-order) mark and buffer pkt n else /*in-order*/
deliver any in-order packets
otherwise:
ignore
receiver
32

## Slide 33
Selective Repeat in Action
33

## Slide 34
Discussion: Efficiency of Selective Repeat
Assume window size W
Assume each packet is lost with probability p
On average, how many packets do we send for each data packet received?
34

## Slide 35: Selective Repeat: Seq# Ambiguity
Example:
seq #’s: 0, 1, 2, 3
window size=3
Error: incorrectly passes duplicate data as new.
35

## Slide 36
State Invariant: Window Location
  Go-back-n (GBN)
  Selective repeat (SR)
sender window
receiver window
sender window
receiver window
36

## Slide 37
Window Location
  Go-back-n (GBN)
  Selective repeat (SR)
sender window
receiver window
sender window
receiver window
Q: what relationship between seq # size and window size?
37

## Slide 38
Sliding Window Protocols: Go-back-n and Selective Repeat
 | Go-back-n | Selective Repeat
data bandwidth: sender to receiver (avg. number of times a pkt is transmitted) |  | 
ACK bandwidth (receiver to sender) |  | 
Relationship between M (the number of seq#) and W (window size) |  | 
Buffer size at receiver |  | 
Complexity |  | 
p: the loss rate of a packet; M: number of seq# (e.g., 3 bit M = 8); W: window size
More efficient
Less efficient
M > W
M ≥ 2W
1
W
Simpler
More complex
Less efficient
More efficient
38

## Slide 39: Question: What is Initial Seq#?
sender
receiver
ACK for 0
accept
data 0
39

## Slide 40: Question: What is Initial Seq#?
sender
receiver
ACK for 0 (n)
accept
data 0 (transfer $1000 to B)
data 0 (transfer $1000 to B)
accept?
40
Notes: a sender should not reuse a seq# before it is sure the packet has left the network

## Slide 41
Outline
Admin and Recap
Reliable data transfer
  perfect channel
  channel with bit errors
  channel with bit errors and losses
  sliding window: reliability with throughput
  connection management
41

## Slide 42: Three Way Handshake (TWH) [Tomlinson 1975]
Host A
SYN(seq=x)
Host B
ACK(seq=x), SYN(seq=y)
ACK(seq=y)
DATA(seq=x+1)
SYN: indicates connection setup
accept data only after
verified y is bounced back
x is the init. seq
notify initial seq#. Accept?
think of y as a challenge
Notes: Syn(seq=x) could be duplicate or malicious

## Slide 43: Scenarios with Duplicate Request/SYN Attack
Host A
Host B
ACK(seq=x), SYN(seq=y)
REJECT(seq=y)
SYN(seq=x)
accept?
no such request
reject

## Slide 44: Scenarios with Duplicate Request/SYN Attack
Host A
Host B
ACK(seq=x), SYN(seq=y)
REJECT(seq=y)
SYN(seq=x)
accept?
no such request
reject
ACK(seq=z)

## Slide 45: Make “Challenge y” Robust
To avoid that “SYNC ACK y” comes from reordering and duplication
  for each connection (sender-receiver pair), ensuring that two identically numbered packets are never outstanding at the same time
    network bounds the life time of each packet
    a sender will not reuse a seq# before it is sure that all packets with the seq# are purged from the network
    seq. number space should be large enough to not limit transmission rate
Notes: Add QUIC design: QUIC uses a cryptographic handshake
  Servers
    front-end servers, which collectively handle billions of requests a day from web browsers and mobile apps across a wide range of services.
  On the client side, we have deployed QUIC in
    Chrome,
    our mobile video streaming YouTube app, and in the
    Google Search app on Android
TCP connections commonly incur at least one round-trip delay of connection setup time before any application data can be sent, and TLS adds two round trips to this delay

## Slide 46: Connection Close
Why connection close?
  so that each side can release resource and remove state about the connection (do not want dangling socket)
client
server
I am done. Are you done too?
I am done too. Goodbye!
init. close
close
close
release
resource?
release
resource?
release
resource?

## Slide 47: General Case: The Two-Army Problem
The gray (blue) armies need to agree on whether or not they will attack the white army. They achieve agreement by sending messengers to the other side. If they both agree, attack; otherwise, no. Note that a messenger can be captured!

## Slide 48: Four Way Teardown
Host A
FIN
Host B
ACK
ACK
FIN
close
close
closed
all states removed
timed wait
can retransmit the ACKif its ACK is lost
closed
A->B closed
A->B closed
all states removed
propose close A->B
propose close B->A

## Slide 49
Outline
Admin and Recap
Reliable data transfer
TCP reliability

## Slide 50
TCP: Overview RFCs: 793, 1122, 1323, 2018, 2581
Point-to-point reliability: one sender, one receiver
Flow controlled and congestion controlled

## Slide 51
Evolution of TCP
Source: http://webcourse.cs.technion.ac.il/236341/Winter2015-2016/ho/WCFiles/Tutorial10.pdf

## Slide 52
Evolution of TCP
Source: http://webcourse.cs.technion.ac.il/236341/Winter2015-2016/ho/WCFiles/Tutorial10.pdf
multiple versions

## Slide 53: TCP Reliable Data Transfer
Connection-oriented:
  connection management
    setup (exchange of control msgs) init’s sender, receiver state before data exchange
    close
Full duplex data:
  bi-directional data flow in same connection
A sliding window protocol
  a combination of go-back-n and selective repeat:
    send & receive buffers
    cumulative acks
    TCP uses a single retransmission timer
    do not retransmit all packets upon timeout

## Slide 54: TCP Segment Structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
rcvr window size
ptr urgent data
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
RST, SYN, FIN:
connection management
(reset, setup teardown
commands)
flow control
ACK: ACK #
valid
counting
by bytes
of data
(not segments!)
Also in UDP
URG: urgent data
(generally not used)
PSH: push data now
(generally not used)

## Slide 55: Flow Control
receive side of a connection has a receive buffer:
speed-matching service: matching the send rate to the receiving app’s drain rate
app process may be slow at reading from buffer
sender won’t overflow
receiver’s buffer by
transmitting too much,
too fast
flow control

## Slide 56: TCP Flow Control: How it Works
spare room in buffer
= RcvWindow
source port #
dest port #
application
data
(variable length)
sequence number
acknowledgement number
rcvr window size
ptr urgent data
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)

## Slide 57
TCP Seq. #’s and ACKs
Seq. #’s:
  byte stream “number” of first byte in segment’s data
ACKs:
  seq # of next byte expected from other side
  cumulative ACK
Host A
Host B
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=42, ACK=80
User
types
‘C’
host ACKs
receipt
of echoed
‘C’
host ACKs
receipt of
‘C’, echoes
back ‘C’
time
simple telnet scenario

## Slide 58: Fast Retransmit
Problem: Timeout period often relatively long:
  long delay before resending lost packet
If sender receives 3 ACKs for the same data, it supposes that segment after ACKed data was lost:
  resend segment before timer expires
Detect lost segments via duplicate ACKs
  sender often sends many segments back-to-back
  if segment is lost, there will likely be many duplicate ACKs

## Slide 59
Triple Duplicate Ack
1
2
3
4
5
6
Packets
Acknowledgements (waiting seq#)
7
2
3
4
4
4
4

## Slide 60: Fast Retransmit:
event: ACK received, with ACK field value of y
if (y > SendBase) {
…
SendBase = y
if (there are currently not-yet-acknowledged segments)
start timer
…
}
else {
increment count of dup ACKs received for y
if (count of dup ACKs received for y = 3) {
resend segment with sequence number y
…
a duplicate ACK for
already ACKed segment
fast retransmit

## Slide 61: TCP: reliable data transfer
00 sendbase = initial_sequence number agreed by TWH
01 nextseqnum = initial_sequence number by TWH
02 loop (forever) {
03 switch(event)
04 event: data received from application above
05 if (window allows send)
06 create TCP segment with sequence number nextseqnum
06 if (no timer) start timer
07 pass segment to IP
08 nextseqnum = nextseqnum + length(data) else put packet in buffer
09 event: timer timeout for sendbase
10 retransmit segment
11 compute new timeout interval
12 restart timer
13 event: ACK received, with ACK field value of y
14 if (y > sendbase) { /* cumulative ACK of all data up to y */
15 cancel the timer for sendbase
sendbase = y
if (no timer and packet pending) start timer for new sendbase
while (there are segments and window allow)
sent a segment;
18 }
19 else { /* y==sendbase, duplicate ACK for already ACKed segment */
20 increment number of duplicate ACKs received for y
21 if (number of duplicate ACKS received for y == 3) {
22 /* TCP fast retransmit */
23 resend segment with sequence number y
24 restart timer for segment y
25 }
26 } /* end of loop forever */
Simplified
TCP
sender

## Slide 62: TCP Receiver ACK Generation [RFC 1122, RFC 2581]
Event at Receiver
Arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
Arrival of in-order segment with
expected seq #. One other
segment has ACK pending
Arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
Arrival of segment that
partially or completely fills gap
TCP Receiver Action
Delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
Immediately send single cumulative
ACK, ACKing both in-order segments
Immediately send duplicate ACK,
indicating seq. # of next expected byte
Immediate send ACK, provided that
segment starts at lower end of gap

## Slide 63
%netstat -t -a
CLOSED
LISTEN
SYN RCVD
SYN
SYN/ACK
ACK
CLOSED
SYN SENT
ESTABLSIHED
ESTABLSIHED
FIN
ACK
ACK
FIN WAIT 1
ESTABLSIHED
ESTABLSIHED
CLOSE WAIT
FIN
LAST ACK
FIN WAIT 2
TIME WAIT

## Slide 64: TCP Connection Management
TCP lifecycle: init SYN/FIN
CLOSED
SYN RCVD
SYN
SYN/ACK
ACK
CLOSED
SYN SENT
ESTABLSIHED
FIN
ACK
ACK
FIN WAIT 1
ESTABLSIHED
ESTABLSIHED
CLOSE WAIT
FIN
LAST ACK
FIN WAIT 2
TIME WAIT
http://dsd.lbl.gov/TCP-tuning/ip-sysctl-2.6.txt

## Slide 65: TCP Connection Management
TCP lifecycle: wait for SYN/FIN
CLOSED
SYN RCVD
SYN
SYN/ACK
ACK
CLOSED
SYN SENT
ESTABLSIHED
FIN
ACK
ACK
FIN WAIT 1
ESTABLSIHED
ESTABLSIHED
CLOSE WAIT
FIN
LAST ACK
FIN WAIT 2
TIME WAIT