## Slide 1: Network Transport Layer: TCP
Qiao Xiang
https://qiaoxiang.me/courses/cnns-xmuf21/index.shtml
11/16/2021
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.

## Slide 2: Admin
Lab assignment 2 to be returned on Nov. 18
Class Project
  15% of your final score
  Please start ASAP
  Talk to the instructor or TA to get feedback

## Slide 3
Recap: Reliable Transport
Basic structure: sliding window protocols
Realization: GBN or SR
General technique: pipelining.

## Slide 4: Recap: Go-Back-N
Sender:
k-bit seq # in pkt header
“window” of up to W, consecutive unack’ed pkts allowed
ACK(n): ACKs all pkts up to, including seq # n - “cumulative ACK”
  note: ACK(n) could mean two things: I have received upto and include n, or I am waiting for n
timer for the packet at base
timeout(n): retransmit pkt n and all higher seq # pkts in window
W
4

## Slide 5
Recap: Go-Back-N
Only state: expectedseqnum
out-of-order pkt:
  discard (don’t buffer) -> no receiver buffering!
  re-ACK pkt with highest in-order seq #
  may generate duplicate ACKs
Wait
udt_send(sndpkt)
default
rdt_rcv(rcvpkt)
&& notcurrupt(rcvpkt)
&& hasseqnum(rcvpkt,expectedseqnum)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(expectedseqnum,ACK,chksum)
udt_send(sndpkt)
expectedseqnum++
expectedseqnum=1
sndpkt =
make_pkt(expectedseqnum,ACK,chksum)
L
5

## Slide 6: Selective Repeat
Sender window
  Window size W: W consecutive unACKed seq #’s
Receiver individually acknowledges correctly received pkts
  buffers out-of-order pkts, for eventual in-order delivery to upper layer
  ACK(n) means received packet with seq# n only
  buffer size at receiver: window size
Sender only resends pkts for which ACK not received
  sender timer for each unACKed pkt
6

## Slide 7: Selective Repeat: Sender, Receiver Windows
W
W
7

## Slide 8: Selective Repeat
data from above :
unACKed packets is less than window size W, send; otherwise block app.
timeout(n):
resend pkt n, restart timer
ACK(n) in [sendbase,sendbase+W-1]:
mark pkt n as received
update sendbase to the first packet unACKed
sender
pkt n in [rcvbase, rcvbase+W-1]
send ACK(n)
if (out-of-order) mark and buffer pkt n else /*in-order*/
deliver any in-order packets
otherwise:
ignore
receiver
8

## Slide 9
Selective Repeat in Action
9

## Slide 10
Discussion: Efficiency of Selective Repeat
Assume window size W
Assume each packet is lost with probability p
On average, how many packets do we send for each data packet received?
10

## Slide 11: Selective Repeat: Seq# Ambiguity
Example:
seq #’s: 0, 1, 2, 3
window size=3
Error: incorrectly passes duplicate data as new.
11

## Slide 12
State Invariant: Window Location
  Go-back-n (GBN)
  Selective repeat (SR)
sender window
receiver window
sender window
receiver window
12

## Slide 13
Window Location
  Go-back-n (GBN)
  Selective repeat (SR)
sender window
receiver window
sender window
receiver window
Q: what relationship between seq # size and window size?
13

## Slide 14: Selective Repeat
data from above :
unACKed packets is less than window size W, send; otherwise block app.
timeout(n):
resend pkt n, restart timer
ACK(n) in [sendbase,sendbase+W-1]:
mark pkt n as received
update sendbase to the first packet unACKed
sender
pkt n in [rcvbase, rcvbase+W-1]
send ACK(n)
if (out-of-order) mark and buffer pkt n else /*in-order*/
deliver any in-order packets
pkt n in [rcvbase-W, rcvbase-1]
send ACK(n)
otherwise:
ignore
receiver
14

## Slide 15
Sliding Window Protocols: Go-back-n and Selective Repeat
 | Go-back-n | Selective Repeat
data bandwidth: sender to receiver (avg. number of times a pkt is transmitted) |  | 
ACK bandwidth (receiver to sender) |  | 
Relationship between M (the number of seq#) and W (window size) |  | 
Buffer size at receiver |  | 
Complexity |  | 
p: the loss rate of a packet; M: number of seq# (e.g., 3 bit M = 8); W: window size
More efficient
Less efficient
M > W
M ≥ 2W
1
W
Simpler
More complex
Less efficient
More efficient
15

## Slide 16
Outline
Admin and Recap
Reliable data transfer
  perfect channel
  channel with bit errors
  channel with bit errors and losses
  sliding window: reliability with throughput
TCP reliability

## Slide 17
TCP: Overview RFCs: 793, 1122, 1323, 2018, 2581
Point-to-point reliability: one sender, one receiver
Flow controlled and congestion controlled

## Slide 18
Evolution of TCP
Source: http://webcourse.cs.technion.ac.il/236341/Winter2015-2016/ho/WCFiles/Tutorial10.pdf

## Slide 19
Evolution of TCP
Source: http://webcourse.cs.technion.ac.il/236341/Winter2015-2016/ho/WCFiles/Tutorial10.pdf
multiple versions

## Slide 20: TCP Reliable Data Transfer
Connection-oriented:
  connection management
    setup (exchange of control msgs) init’s sender, receiver state before data exchange
    close
Full duplex data:
  bi-directional data flow in same connection
A sliding window protocol
  a combination of go-back-n and selective repeat:
    send & receive buffers
    cumulative acks
    TCP uses a single retransmission timer
    do not retransmit all packets upon timeout

## Slide 21: TCP Segment Structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
rcvr window size
ptr urgent data
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
RST, SYN, FIN:
connection management
(reset, setup teardown
commands)
flow control
ACK: ACK #
valid
counting
by bytes
of data
(not segments!)
Also in UDP
URG: urgent data
(generally not used)
PSH: push data now
(generally not used)

## Slide 22
Outline
Admin and Recap
Reliable data transfer
  perfect channel
  channel with bit errors
  channel with bit errors and losses
  sliding window: reliability with throughput
TCP reliability
  data seq#, ack, buffering

## Slide 23: Flow Control
receive side of a connection has a receive buffer:
speed-matching service: matching the send rate to the receiving app’s drain rate
app process may be slow at reading from buffer
sender won’t overflow
receiver’s buffer by
transmitting too much,
too fast
flow control

## Slide 24: TCP Flow Control: How it Works
spare room in buffer
= RcvWindow
source port #
dest port #
application
data
(variable length)
sequence number
acknowledgement number
rcvr window size
ptr urgent data
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)

## Slide 25
TCP Seq. #’s and ACKs
Seq. #’s:
  byte stream “number” of first byte in segment’s data
ACKs:
  seq # of next byte expected from other side
  cumulative ACK in standard header
  selective ACK in options
Host A
Host B
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=42, ACK=80
User
types
‘C’
host ACKs
receipt
of echoed
‘C’
host ACKs
receipt of
‘C’, echoes
back ‘C’
time
simple telnet scenario

## Slide 26: TCP Send/Ack Optimizations
TCP includes many tune/optimizations, e.g.,
  the “small-packet problem”: sender sends a lot of small packets (e.g., telnet one char at a time)
    Nagle’s algorithm: do not send data if there is small amount of data in send buffer and there is an unack’d segment
  the ”ack inefficiency” problem: receiver sends too many ACKs, no chance of combing ACK with data
    Delayed ack to reduce # of ACKs/combine ACK with reply

## Slide 27: TCP Receiver ACK Generation [RFC 1122, RFC 2581]
Event at Receiver
Arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
Arrival of in-order segment with
expected seq #. One other
segment has ACK pending
Arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
Arrival of segment that
partially or completely fills gap
TCP Receiver Action
Delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
Immediately send single cumulative
ACK, ACKing both in-order segments
Immediately send duplicate ACK,
indicating seq. # of next expected byte
Immediate send ACK, provided that
segment starts at lower end of gap

## Slide 28
Outline
Admin and Recap
Reliable data transfer
  perfect channel
  channel with bit errors
  channel with bit errors and losses
  sliding window: reliability with throughput
TCP reliability
  data seq#, ack, buffering
  timeout realization

## Slide 29
TCP Reliable Data Transfer
Basic structure: sliding window protocol
Remaining issue: How to determine the “right” parameters?
  timeout value?
  sliding window size?

## Slide 30
History
Key parameters for TCP in mid-1980s
  fixed window size W
  timeout value = 2 RTT
Network collapse in the mid-1980s
  UCB  LBL throughput dropped by 1000X !
The intuition was that the collapse was caused by wrong parameters…

## Slide 31: Timeout: Cost of Timeout Param
Why is good timeout value important?
too short
  premature timeout
  unnecessary retransmissions; many duplicates
too long
  slow reaction to segment loss
Q: Is it possible to set Timeout as a constant?
Q: Any problem w/ the early approach: Timeout = 2 RTT

## Slide 32: Setting Timeout
Problem:
Ideally, we set timeout = RTT, but RTT is not a fixed value => using the average of RTT will generate many timeouts due to network variations
Possibility: using the average/median of RTT
Issue: this will generate many timeouts due to network variations
Solution:
Set Timeout RTO = avg + “safety margin” based on variation
Timeout = EstRTT + 4 * DevRTT
TCP approach:
RTT
freq.

## Slide 33: Compute EstRTT and DevRTT
EstRTT = (1-alpha)*EstRTT + alpha*SampleRTT
Exponential weighted moving average (EWMA)
  influence of past sample decreases exponentially fast
- SampleRTT: measured time from segment transmission until ACK receipt
- typical value: alpha = 0.125
DevRTT = (1-beta)*DevRTT + beta|SampleRTT-EstRTT|
(typically, beta = 0.25)

## Slide 34: An Example TCP Session

## Slide 35: Fast Retransmit
Issue: Timeout period often relatively long:
  long delay before resending lost packet
Question: Can we detect loss faster than RTT?
If sender receives 3 ACKs for the same data, it supposes that segment after ACKed data was lost:
  resend segment before timer expires
Detect lost segments via duplicate ACKs
  sender often sends many segments back-to-back
  if segment is lost, there will likely be many duplicate ACKs

## Slide 36
Triple Duplicate Ack
1
2
3
4
5
6
Packets
Acknowledgements (waiting seq#)
7
2
3
4
4
4
4

## Slide 37: Fast Retransmit:
event: ACK received, with ACK field value of y
if (y > SendBase) {
…
SendBase = y
if (there are currently not-yet-acknowledged segments)
start timer
…
}
else {
increment count of dup ACKs received for y
if (count of dup ACKs received for y = 3) {
resend segment with sequence number y
…
a duplicate ACK for
already ACKed segment
fast retransmit

## Slide 38: TCP: reliable data transfer
00 sendbase = initial_sequence number agreed by TWH
01 nextseqnum = initial_sequence number by TWH
02 loop (forever) {
03 switch(event)
04 event: data received from application above
05 if (window allows send)
06 create TCP segment with sequence number nextseqnum
06 if (no timer) start timer
07 pass segment to IP
08 nextseqnum = nextseqnum + length(data) else put packet in buffer
09 event: timer timeout for sendbase
10 retransmit segment
11 compute new timeout interval
12 restart timer
13 event: ACK received, with ACK field value of y
14 if (y > sendbase) { /* cumulative ACK of all data up to y */
15 cancel the timer for sendbase
sendbase = y
if (no timer and packet pending) start timer for new sendbase
while (there are segments and window allow)
sent a segment;
18 }
19 else { /* y==sendbase, duplicate ACK for already ACKed segment */
20 increment number of duplicate ACKs received for y
21 if (number of duplicate ACKS received for y == 3) {
22 /* TCP fast retransmit */
23 resend segment with sequence number y
24 restart timer for segment y
25 }
26 } /* end of loop forever */
Simplified
TCP
sender

## Slide 39
Outline
Admin and Recap
Reliable data transfer
  perfect channel
  channel with bit errors
  channel with bit errors and losses
  sliding window: reliability with throughput
TCP reliability
  data seq#, ack, buffering
  timeout realization
  connection management

## Slide 40: Why Connection Setup/When to Accept (Safely Deliver) First Packet?
sender
receiver
ACK for 0
accept
data 0
40

## Slide 41: Why Connection Setup/When to Accept (Safely Deliver) First Packet?
sender
receiver
ACK for 0 (n)
accept
data 0 (transfer $1000 to B)
data 0 (transfer $1000 to B)
accept?
41
Notes: a sender should not reuse a seq# before it is sure the packet has left the network

## Slide 42: Transport “Safe-Setup” Principle
A general safety principle for a receiver R to accept a message from a sender S is the general “authentication” principle, which consists of two conditions:
  Transport authentication principle:
  [p1] Receiver can be sure that what Sender says is fresh
  [p2] Receiver receives something that only Sender can say
We first assume a secure setting: no malicious attacks.
Exercise: Techniques to allow a receiver to check for freshness (e.g., add a time stamp)?

## Slide 43: Generic Challenge-Response Structure Checking Freshness
sender
receiver
Challenge (nonce)
deliver
I have data to send
Demonstrate knowing nonce; data

## Slide 44: Three Way Handshake (TWH) [Tomlinson 1975]
Host A
SYN(seq=x)
Host B
ACK(seq=x), SYN(seq=y)
ACK(seq=y)
DATA(seq=x+1)
SYN: indicates connection setup
accept data only after
verified y is bounced back
x is the init. seq
notify initial seq#. Accept?
think of y as a challenge
Notes: Syn(seq=x) could be duplicate or malicious

## Slide 45: Scenarios with Duplicate Request/SYN Attack
Host A
Host B
ACK(seq=x), SYN(seq=y)
REJECT(seq=y)
SYN(seq=x)
accept?
no such request
reject

## Slide 46: Scenarios with Duplicate Request/SYN Attack
Host A
Host B
ACK(seq=x), SYN(seq=y)
REJECT(seq=y)
SYN(seq=x)
accept?
no such request
reject
ACK(seq=z)

## Slide 47: Make “Challenge y” Robust
To avoid that “SYNC ACK y” comes from reordering and duplication
  for each connection (sender-receiver pair), ensuring that two identically numbered packets are never outstanding at the same time
    network bounds the life time of each packet
    a sender will not reuse a seq# before it is sure that all packets with the seq# are purged from the network
    seq. number space should be large enough to not limit transmission rate
Increasingly move to cryptographic challenge and response
Notes: Add QUIC design: QUIC uses a cryptographic handshake
  Servers
    front-end servers, which collectively handle billions of requests a day from web browsers and mobile apps across a wide range of services.
  On the client side, we have deployed QUIC in
    Chrome,
    our mobile video streaming YouTube app, and in the
    Google Search app on Android
TCP connections commonly incur at least one round-trip delay of connection setup time before any application data can be sent, and TLS adds two round trips to this delay

## Slide 48: Connection Close
Why connection close?
  so that each side can release resource and remove state about the connection (do not want dangling socket)
client
server
I am done. Are you done too?
I am done too. Goodbye!
init. close
close
close
release
resource?
release
resource?
release
resource?

## Slide 49: General Case: The Two-Army Problem
The gray (blue) armies need to agree on whether or not they will attack the white army. They achieve agreement by sending messengers to the other side. If they both agree, attack; otherwise, no. Note that a messenger can be captured!

## Slide 50: Time_Wait
Generic technique: Timeout to “solve” infeasible problem
  Instead of message-driven state transition, use a timeout based transition; use timeout to handle error cases
client
server
I am done. Are you done too?
I am done too. Goodbye!
init. close
close
close
release
resource?
release
resource?
release
resource?
Closed
Working
Time_Waiit
Working
Closed

## Slide 51: Time_Wait Design Options
Time to retransmit ACK
Host A
FIN
Host B
ACK
close
Design 2 (receiver time wait)
Close after first ACK
All states removed
All states removed
Host A
FIN
Host B
ACK
close
Time = n x timeout
Time to retry FIN after each timeout
Design 1 (initiator time wait)
Close after receive FIN
All states removed
All states removed

## Slide 52: TCP Four Way Teardown (For Bi-Directional Transport)
Host A
FIN
Host B
ACK
ACK
FIN
close
close
closed
all states removed
timed wait
can retransmit the ACKif its ACK is lost
closed
A->B closed
A->B closed
all states removed
propose close A->B
propose close B->A

## Slide 53
%netstat -t -a
CLOSED
LISTEN
SYN RCVD
SYN
SYN/ACK
ACK
CLOSED
SYN SENT
ESTABLSIHED
ESTABLSIHED
FIN
ACK
ACK
FIN WAIT 1
ESTABLSIHED
ESTABLSIHED
CLOSE WAIT
FIN
LAST ACK
FIN WAIT 2
TIME WAIT

## Slide 54: TCP Connection Management
TCP lifecycle: init SYN/FIN
CLOSED
SYN RCVD
SYN
SYN/ACK
ACK
CLOSED
SYN SENT
ESTABLSIHED
FIN
ACK
ACK
FIN WAIT 1
ESTABLSIHED
ESTABLSIHED
CLOSE WAIT
FIN
LAST ACK
FIN WAIT 2
TIME WAIT
http://dsd.lbl.gov/TCP-tuning/ip-sysctl-2.6.txt

## Slide 55: TCP Connection Management
TCP lifecycle: wait for SYN/FIN
CLOSED
SYN RCVD
SYN
SYN/ACK
ACK
CLOSED
SYN SENT
ESTABLSIHED
FIN
ACK
ACK
FIN WAIT 1
ESTABLSIHED
ESTABLSIHED
CLOSE WAIT
FIN
LAST ACK
FIN WAIT 2
TIME WAIT

## Slide 56
A Summary of Questions
Basic structure: sliding window protocols
How to determine the “right” parameters?
  timeout: mean + variation
  sliding window size?

## Slide 57
Sliding Window Size Function: Rate Control
Transmission rate determined by congestion window size, cwnd, over segments:
cwnd segments, each with MSS bytes sent in one RTT:
Rate =
cwnd * MSS
RTT
Bytes/sec
cwnd
Assume W is small enough. Ignore small details. MSS: Minimum Segment Size

## Slide 58
Some General Questions
Big picture question:
How to determine a flow’s sending rate?
For better understanding, we need to look at a few basic questions:
What is congestion (cost of congestion)?
Why are desired properties of congestion control?

## Slide 59
Roadmap
What is congestion
The basic CC alg
TCP/reno CC
TCP/Vegas
A unifying view of TCP/Reno and TCP/Vegas
Network wide resource allocation
  Framework
  Axiom derivation of network-wide objective function
  Derive distributed algorithm

## Slide 60
Outline
Admin and recap
Setting timeout
Transport congestion control
  what is congestion (cost of congestion)

## Slide 61
flow 2 (5 Mbps)
flow 1
router 1
router 2
10 Mbps
5 Mbps
20 Mbps
Cause/Cost of Congestion: Single Bottleneck
- Flow 2 has a fixed sending rate of 5 Mbps
- We vary the sending rate of flow 1 from 0 to 20 Mbps
- Assume
  no retransmission; link from router 1 to router 2 has infinite buffer
20 Mbps
20 Mbps
throughput: e2e packets delivered in unit time
Delay?
sending rate by flow 1 (Mbps)
throughput of flow 1 & 2 (Mbps)
5
10
5
0
sending rate by flow 1 (Mbps)
delay at central link
5
0
delay due to
randomness

## Slide 62
flow 2 (5 Mbps)
flow 1
router 1
10 Mbps
5 Mbps
20 Mbps
Cause/Cost of Congestion: Single Bottleneck
Assume
  no retransmission
  the link from router 1 to router 2 has finite buffer
  throughput: e2e packets delivered in unit time
20 Mbps
20 Mbps
Zombie packet: a packet dropped at the link from router 2 to router 5; the upstream transmission from router 1 to router 2 used for that packet was wasted!
router 3
router 4
router 2
router 5
router 6
sending rate by flow 1 (Mbps)
throughput of flow 1 & 2 (Mbps)
5
10
5
0
x

## Slide 63
Summary: The Cost of Congestion
When sources sending rate too high for the network to handle”:
Packet loss =>
  wasted upstream bandwidth when a pkt is discarded at downstream
  wasted bandwidth due to retransmission (a pkt goes through a link multiple times)
High delay
Load
Load
Delay
Throughput
knee
cliff
congestion
collapse
packet
loss

## Slide 64
Outline
Admin and recap
Setting timeout
Transport congestion control
  what is congestion (cost of congestion)
  basic congestion control alg.

## Slide 65
The Desired Properties of a Congestion Control Scheme
Efficiency: close to full utilization but low delay
  fast convergence after disturbance
Fairness (resource sharing)
Distributedness (no central knowledge for scalability)

## Slide 66: Derive CC: A Simple Model
User 1
User 2
User n
sum xi
d = sum xi > Xgoal?
x1
x2
xn
Flows observe congestion signal d, and locally take actions to adjust rates.

## Slide 67
Linear Control
Proposed by Chiu and Jain (1988)
The simplest control strategy
Discussion: values of the parameters?

## Slide 68
State Space of Two Flows
x2
x1
overload
underload
efficiency line: x1+x2=C
fairness line: x1=x2
x(0)

## Slide 69
x0
efficiency
efficiency: distributed linear rule
x0
intersection
x0
congestion
fairness
x0

## Slide 70: Implication: Congestion (overload) Case
In order to get closer to efficiency and fairness after each update, decreasing of rate must be multiplicative decrease (MD)
  aD = 0
  bD < 1

## Slide 71
efficiency: distributed linear rule
x0
no-congestion
x0
efficiency
fairness
x0
convergence
x0

## Slide 72: Implication: No Congestion Case
In order to get closer to efficiency and fairness after each update, additive and multiplicative increasing (AMI), i.e.,
  aI > 0, bI > 1
Simply additive increase gives better improvement in fairness (i.e., getting closer to the fairness line)
Multiplicative increase may grow faster

## Slide 73
Intuition: State Trace Analysis of Four Special Cases
 | Additive Decrease | Multiplicative Decrease
Additive Increase | AIAD (bI=bD=1) | AIMD (bI=1, aD=0)
Multiplicative Increase | MIAD (aI=0, bI>1, bD=1) | MIMD (aI=aD=0)
Discussion: state transition trace.

## Slide 74
AIMD: State Transition Trace
x1
x2
x0
fairness line: x1=x2
efficiency line: x1+x2=C
overload
underload

## Slide 75: Intuition: Another Look
Consider the difference or ratio of the rates of two flows
  AIAD
  MIMD
  MIAD
  AIMD
Notes: AIAD: difference does not change
MIMD: ratio does not change
MIAD: difference becomes bigger
AIMD: difference does not change

## Slide 76: Mapping A(M)I-MD to Protocol
Question to look at: How do we apply the A(M)I-MD algorithm?
Notes: Implement d(t): loss/delay
Adjust window size
b_D: exponential backoff timeout after window size is 1

## Slide 77
Window-based:
Congestion control by controlling the window size of a transport scheme, e.g., set window size to 64KBytes
Example: TCP
Rate-based:
Congestion control by explicitly controlling the sending rate of a flow, e.g., set sending rate to 128Kbps
Example: ATM
Discussion: rate-based vs. window-based
Rate-based vs. Window-based

## Slide 78
Window-based Congestion Control
Window-based congestion control is self-clocking: considers flow conservation, and adjusts to RTT variation automatically.
Hence, for better safety, more designs use window-based design.

## Slide 79: Mapping A(M)I-MD to Protocol
Question to look at: How do we apply the A(M)I-MD algorithm?
Notes: Implement d(t): loss/delay
Adjust window size
b_D: exponential backoff timeout after window size is 1

## Slide 80
Outline
Admin and recap
Setting timeout
Transport congestion control
  what is congestion (cost of congestion)
  basic congestion control alg.
  TCP/reno congestion control

## Slide 81
TCP Congestion Control
Closed-loop, end-to-end, window-based congestion control
Designed by Van Jacobson in late 1980s, based on the AIMD alg. of Dah-Ming Chu and Raj Jain
Worked in a large range of bandwidth values: the bandwidth of the Internet has increased by more than 200,000 times
Many versions
  TCP/Tahoe: this is a less optimized version
  TCP/Reno: many OSs today implement Reno type congestion control
  TCP/Vegas: not currently used
For more details: see TCP/IP illustrated; or read http://lxr.linux.no/source/net/ipv4/tcp_input.c for linux implementation

## Slide 82
Basic Structure
Two “phases”
  MI: slow-start
  AIMD: congestion avoidance
Important variables:
  cwnd: congestion window size
  ssthresh: threshold between the slow-start phase and the congestion avoidance phase

## Slide 83: Visualization of the Two Phases

## Slide 84
MI: Slow Start
Algorithm: MI
  double cwnd every RTT until network congested
  Goal: getting to equilibrium gradually but quickly, to get a rough estimate of the optimal of cwnd

## Slide 85
MI: Slow-start
ACK for segment 1
segment 1
cwnd = 1
cwnd = 2
segment 2
segment 3
ACK for segments 2 + 3
cwnd = 4
segment 4
segment 5
segment 6
segment 7
cwnd = 6
Initially:
cwnd = 1;
ssthresh = infinite (e.g., 64K);
For each newly ACKed segment:
if (cwnd < ssthresh)
/* MI: slow start*/
cwnd = cwnd + 1;
cwnd = 8

## Slide 86: Startup Behavior with Slow-start
See [Jac89]

## Slide 87: AIMD: Congestion Avoidance
Algorithm: AIMD
  increases window by 1 per round-trip time (how?)
  cuts window size
    to half when detecting congestion by 3DUP
    to 1 if timeout
    if already timeout, doubles timeout
    Goal: Maintains equilibrium and reacts around equilibrium

## Slide 88
TCP/Reno Full Alg
Initially:
cwnd = 1;
ssthresh = infinite (e.g., 64K);
For each newly ACKed segment:
if (cwnd < ssthresh) // slow start: MI
cwnd = cwnd + 1;
else
// congestion avoidance; AI cwnd += 1/cwnd;
Triple-duplicate ACKs:
// MD
cwnd = ssthresh = cwnd/2;
Timeout:
ssthresh = cwnd/2; // reset
cwnd = 1;
(if already timed out, double timeout value; this is called exponential backoff)