## Slide 1: Statistical Multiplexing; Layered Network Architecture; End-to-end Arguments
Qiao Xiang
https://qiaoxiang.me/courses/cnns-xmuf21/index.shtml
09/23/2021
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.

## Slide 2
Outline
Admin. and recap
A taxonomy of communication networks
Layered network architecture

## Slide 3: Admin.
Readings from the textbook and additional suggested readings
  All are highly recommended
  Some are marked as required
Assignment one is linked on the schedule page
  Oct. 14, in class or by email to the instructor

## Slide 4: Recall: Internet Physical Infrastructure
Backbone ISP
ISP
ISP
Residential access, e.g.,
  Cable, Fiber, DSL, Wireless
Campus access, e.g.,
  Ethernet, Wireless
The Internet is a network of networks
Each individually administrated network is called an Autonomous System (AS)
  ~ 58000 ASes; Avg 5.7 hops; (http://bgp.potaroo.net/as2.0/bgp-active.html)
data center

## Slide 5: Recap: Challenges - Scale
“Developers who have worked at the small scale might be asking themselves why we need to bother when we could just use some kind of out-of the-box solution. For small-scale applications, this can be a great idea. We save time and money up front and get a working and serviceable application. The problem comes at larger scales—there are no off-the-shelf kits that will allow you to build something like Amazon... There’s a good reason why the largest applications on the Internet are all bespoke creations: no other approach can create massively scalable applications within a reasonable budget.”
http://www.evontech.com/symbian/55.html

## Slide 6: Recap: Challenges - General Complexity
Complexity in highly organized systems arises primarily from design strategies intended to create robustness to uncertainty in their environments and component parts.
  Scalability is robustness to changes to the size and complexity of a system as a whole.
  Evolvability is robustness of lineages to large changes on various (usually long) time scales.
  Reliability is robustness to component failures.
  Efficiency is robustness to resource scarcity.
  Modularity is robustness to component rearrangements.
David Meyer

## Slide 7: Recap: Challenges – Distributed vs Centralized
Distributed computing is hard, e.g.,
  FLP Impossibility Theorem
  Arrow’s Impossibility Theorem
Achieved good design for only few specific tasks (e.g., state distribution, leader election). Hence, a trend in networking is Software Defined Networking, which is a way of moving away from generic distributed computing, by focusing on utilizing the few well-understood primitives, in particular logically centralized state.

## Slide 8
Basic question: how are data (the bits) transferred through communication networks?
Recap: A Taxonomy of Comm. Networks
communication networks
switched networks
broadcast networks
circuit-switched networks (e.g. telephone, GSM)
packet-switched networks (e.g. Internet)

## Slide 9
Outline
Admin. and recap
A taxonomy of communication networks
  circuit switched networks

## Slide 10
Circuit Switching
Each link has a number of “circuits”
  sometime we refer to a “circuit” as a channel or a line
An end-to-end connection reserves one “circuit” at each link
First commercial telephone switchboard was opened in 1878 to serve the 21 telephone customers in New Haven
Notes: http://www.classicrotaryphones.com/new-england-operators2_big.jpg

## Slide 11: Circuit Switching: The Process
Three phases
  circuit establishment
  data transfer
  circuit termination

## Slide 12
circuit establishment
DATA
data transmission
circuit termination
Host A
Host B
Node 1
Node 2
propagation delay
from A to Node 1
propagation delay
from B To A
processing delay at Node 1
Timing Diagram of Circuit Switching

## Slide 13
Delay Calculation in Circuit Switched Networks
Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x105 km/sec)
Propagation delay: delay for the first bit to go from a source to a destination
DATA
prop. delay: d/s

## Slide 14
Delay Calculation in Circuit Switched Networks
Transmission delay:
R = reserved bandwidth (bps)
L = message length (bits)
DATA
d/s
trans. delay = L/R
Transmission delay: time to pump data onto link at line rate

## Slide 15: An Example
Propagation delay
  suppose the distance between A and B is 4000 km, then one-way propagation delay is:
Transmission delay
  suppose your iphone reserves a one-slot HSCSD channel
    each HSCSD frame can transmit about 115 kbps
    a frame is divided into 8 slots
  then the transmission delay of using one reserved slot for a message of 1 Kbits:

## Slide 16: An Example (cont.)
Suppose the setup message is very small, and the total setup processing delay is 200 ms
Then the delay to transfer a message of 1 Kbits from A to B (from the beginning until host receives last bit) is:
DATA
20 + 200
20
20
70

## Slide 17
Outline
Admin. and recaps
A brief introduction to the Internet: past and present
Challenges of Internet networks and apps
A taxonomy of communication networks
  circuit switched networks
  packet switched networks

## Slide 18
Packet Switching
Each end-to-end data flow (i.e., a sender-receiver pair) divided into packets
Packets have the following structure:
    header and trailer carry control information (e.g., destination address, check sum)
    where is the control information for circuit switching?
At each node the entire packet is received, processed (e.g., routing), stored briefly, and then forwarded to the next node; thus packet-switched networks are also called store-and-forward networks. On its turn, a packet uses full link bandwidth
Header
Data
Trailer

## Slide 19
Packet Switching

## Slide 20
Inside a Packet Switching Router
An output queueing switch
incoming links
outgoing links
node
Memory

## Slide 21
Outline
Admin. and recaps
A brief introduction to the Internet: past and present
Challenges of Internet networks and apps
A taxonomy of communication networks
  circuit switched networks
  packet switched networks
  circuit switching vs. packet switching

## Slide 22
Packet Switching vs. Circuit Switching
The early history of the Internet was a heated debate between Packet Switching and Circuit Switching
  the telephone network was the dominant network
Need to compare packet switching with circuit switching

## Slide 23: Circuit Switching vs. Packet Switching
 | circuit switching | packet switching
resource usage | use a single partition bandwidth | use whole link bandwidth
reservation/setup | need reservation (setup delay) | no reservation
resource contention | busy signal (session loss) | congestion (long delay and packet losses)
charging | time | packet
header | no per-pkt header | per packet header
fast path processing | fast | per packet processing

## Slide 24: Circuit Switching vs. Packet Switching
 | circuit switching | packet switching
resource usage | use a single partition bandwidth | use whole link bandwidth
reservation/setup | need reservation (setup delay) | no reservation
resource contention | busy signal (session loss) | congestion (long delay and packet losses)
charging | time | packet
header | no per-pkt header | per packet header
fast path processing | fast | per packet processing

## Slide 25: Key Issue to be Settled
A key issue: what is the efficiency of resource partition?
Tool used to analyze the issue: queueing theory
  Some basic results of queueing theory can be quite useful in many systems settings
10G
5G
5G
Notes: 10M bps link and 10 flows: partition into 10 1 Mbps or

## Slide 26
Outline
Admin. and recaps
A brief introduction to the Internet: past and present
Challenges of Internet networks and apps
A taxonomy of communication networks
  circuit switched networks
  packet switched networks
  circuit switching vs. packet switching
  M/M queues and statistical multiplexing

## Slide 27: Queueing Theory
Strategy:
  model system state
    if we know the fraction of time that the system spends at each state, we can get answers to many basic questions: how long does a new request need to wait before being served?
System state changes upon events:
  introduce state transition diagram
  focus on equilibrium: state trend neither growing nor shrinking (key issue: how to define equilibrium)
Our approach: We are not interested in extremely precise modeling, but want quantitative intuition

## Slide 28: Warm up: Analysis of Circuit-Switching Blocking (Busy) Time
Assume a link has only a finite number of N circuits
Objective: compute the percentage of time that a new session (call) is blocked
Analogy in a more daily-life scenario?
Key parameters?
Notes: Key input parameters?

## Slide 29: Analysis of Circuit-Switching Blocking (Busy) Time
Consider a simple arrival pattern
  client requests arrive at a rate of  (lambda/second)
  service rate: each call takes on average 1/ second
Arrival and service patterns: memoryless (Markovian)
  During a small interval t, the number of expected new arrivals is: t
  During a small interval t, the chance (fraction) of a current call finishes is: t
This model is also called an M/M/N model

## Slide 30: Analysis of Circuit-Switching Blocking (Busy) Time: State
k+1
system state: # of busy lines
0
1
k
N
p0
p1
pk
pk+1
pN
Q: How to characterize equilibrium?

## Slide 31: Equilibrium = Time Reversibility [Frank Kelly]
Statistically cannot distinguish
time
state
k
k+1
=
=
=
Play the sequence backwards

## Slide 32: Analysis of Circuit-Switching Blocking (Busy) Time: Sketch
0
1
k
N
system state: # of busy lines
at equilibrium (time resersibility) in one unit time: #(transitions k  k+1) = #(transitions k+1  k)
p0
p1
pk
k+1
pk+1

(k+1)
pN

## Slide 33: Queueing Analysis: Packet Switching Delay
Four types of delay at each hop
  nodal processing delay: check errors & routing
  queueing: time waiting for its turn at output link
  transmission delay: time to pump packet onto a link at link speed
  propagation delay: router to router propagation
The focus is on queueing and transmission delay
system state?

## Slide 34: Packet Switching Delay
0
1
k
N
system state: #packets in queue
at equilibrium (time reversibility) in one unit time: #(transitions k  k+1) = #(transitions k+1  k)
p0
p1
pk
k+1
pk+1



## Slide 35: Summary: Queueing Theory
Model system state
Introduce state transition diagram
Focus on equilibrium: state trend neither growing nor shrinking

## Slide 36: Example
Assume requests (packets) come in at a rate of one request per 50 ms
Each request (packet) takes on average 20 ms
What is the fraction of time that the system is empty?
What is the chance that a packet newly arrived needs to wait for 3 early packets?
=1/50ms =20/s
=20 ms, =50/s
Notes: Rau = 2/3
(1-2/3)(2/3)^3 = 1/3 * 8/27 = 8/84 = 10%

## Slide 37: Analysis of Delay (cont’)
Average queueing delay:
Transmission delay:
Queueing + transmission:
0
1
k
k+1



## Slide 38
Delay
For a demo of M/M/1, see: http://www.dcs.ed.ac.uk/home/jeh/Simjava/queueing/mm1_q/mm1_q.html

## Slide 39
Queueing Delay as a Function of Utilization
 ~ 0: average queueing delay small
 -> 1: delay becomes large
 > 1: more “work” arriving than can be serviced, average delay infinite !

Assume:
R = link bandwidth (bps)
L = packet length (bits)
S = L / R
a = average packet arrival rate (pkt/sec)

## Slide 40: Statistical Multiplexing
no reservation: all arrivals into the single link, the queueing delay + transmission delay:
reservation: each flow uses its own reserved (sub)link with rate /n, the queueing delay + transmission delay:
A simple model to compare bandwidth efficiency of
- reservation/dedication (aka circuit-switching) vs
- no reservation (aka packet switching) setup
- a single bottleneck link with
service rate
- flows; each flow has an arrival rate of
For each flow i:

## Slide 41
Summary: Packet Switching vs. Circuit Switching
Advantages of packet switching over circuit switching
  most important advantage of packet-switching over circuit switching is statistical multiplexing, and therefore more efficient bandwidth usage
Disadvantages of packet switching
  potential congestion: packet delay and high loss
    protocols needed for reliable data transfer, congestion control
    it is possible to guarantee quality of service (QoS) in packet-switched networks and still gain statistical multiplexing, but it adds much complexity
  packet header overhead
  per packet processing overhead

## Slide 42
Outline
Admin. and recap
A taxonomy of communication networks
  circuit switched networks
  packet switched networks
  circuit switching vs. packet switching
  datagram and virtual circuit packet switched networks

## Slide 43
A Taxonomy of Packet-Switched Networks According to Routing
Two types of packet switching
  datagram network
    each packet of a flow is switched independently
  virtual circuit network:
    all packets from one flow are sent along a pre-established path (= virtual circuit)

## Slide 44: Datagram Packet Switching
Commonly when we say packet switching we mean datagram switching
Example: IP networks
Each packet is independently switched
  each packet header contains complete destination address
  receiving a packet, a router looks at the packet’s destination address and searches its current routing table to determine the possible next hops, and pick one
Analogy: postal mail system
Notes:   Disadvantages: routes may change during session
  Advantage: routers do not keep any state about a flow;
  thus, network architecture is
    robust
    scalable

## Slide 45
Host A
Host B
Host E
Host D
Host C
Node 1
Node 2
Node 3
Node 4
Node 5
Node 6
Node 7
Datagram Packet Switching

## Slide 46: Timing Diagram of Datagram Switching
Packet 1
Packet 2
Packet 3
Packet 1
Packet 2
Packet 3
Packet 1
Packet 2
Packet 3
Host A
Host B
Node 1
Node 2
propagation
delay from
Host A to
Node 1
transmission
time of Packet 1
at Host A

## Slide 47: Virtual-Circuit Packet Switching
Example: Multiple Label Packet Switching (MPLS) in IP networks
Hybrid of circuit switching and datagram switching
  fixed path determined at virtual circuit setup time, remains fixed thru flow
  Implementation:
    each packet carries a short local, tag (virtual-circuit (VC) #); tag determines next hop
Incoming VC# | Outgoing Interface | QoS
12 | 2 | 
16 | 3 | 
20 | 3 | 
… |  | 

## Slide 48
Host A
Host B
Host E
Host D
Host C
Node 1
Node 2
Node 3
Node 4
Node 5
Node 6
Node 7
Virtual-Circuit Switching

## Slide 49: Virtual-Circuit Packet Switching
Three phases
  VC establishment
  Data transfer
  VC disconnect

## Slide 50: Timing Diagram of Virtual-Circuit Switching
Packet 1
Packet 2
Packet 3
Packet 1
Packet 2
Packet 3
Packet 1
Packet 2
Packet 3
Host 1
Host 2
Node 1
Node 2
propagation delay
between Host 1
and Node 1
VC
establishment
VC
termination
data
transfer

## Slide 51: Discussion: Datagram Switching vs. Virtual Circuit Switching
What are the benefits of datagram switching over virtual circuit switching?
What are the benefits of virtual circuit switching over datagram switching?
Notes: What advantages do virtual circuit have over datagram?
can treat different flows differently, if flows setup its desired treatment
  Guarantees in-sequence delivery of packets
  However: Packets from different virtual circuits may be interleaved

## Slide 52
Summary of the Taxonomy of Communication Networks
circuit-switched network
communication network
switched network
broadcast communication
packet-switched network
datagram network
virtual circuit network

## Slide 53: Summary of Progress
We have seen the hardware infrastructure, the basic communication scheme, a next key question is how to develop the software system.